## Slide 2: Trend and Research Progress of refrigerant valves for New Energy Vehicles

## Slide 3: Single cooling system
Single cooling system
Representative car models:
***
***
Battery air-cooled or natural-cooled
Typical components: TXV Water pump Water Valve
Compressor
EXV
Blower
Evaporator
Fluid storage tank
Condenser
Fan
Heater core
Water Pump
Evaporator
Fan
Gas-liquid separator
Compressor
EXV
Condenser (outboard heat exchanger)
High pressure gas
High pressure liquid
Low pressure gas
Low pressure gas

## Slide 4: Battery liquid cooling or direct cooling
Single cooling system
Representative models:
***
***
Battery liquid cooling or direct cooling
Typical components:
TXV+SOV
So-TXV
EXV
water pump Valve
Kettle
Electric compressor
Kettle
Electric water pump
Motor assembly
Electric water pump
Electric 3-way proportional valve
Electric water pump
Heat Exchanger
Heater core
Coolant
Refrigerant

## Slide 5
Heat pumps
Representative models:
Leaf
BYD ***
BYD ***
Battery liquid cooling or direct cooling
Typical components:EXV
SOV
FBEV
Water Pump Water Valve
Heat pumps

## Slide 6
Heat pumps
Representative models:
Leaf
BYD ***
BYD ***
Battery liquid cooling or direct cooling
Typical components:EXV
SOV
FBEV
Water Pump Water Valve

## Slide 7
Check Valve 3
Evaporator
Internal condenser
Battery Cold Plate
Front condenser
Radiator
Kettle
Electric drive
Pump
Chiller
(Waste heat recovery device)
3-way valve
Check Valve 1
Check Valve 2
Battery Cold Plate
Gas-liquid separator

## Slide 8: Indirect heat pumps
Indirect heat pumps
Representative models:
J***
Z***
B***
***
Battery liquid cooling or direct cooling
Typical components:
EXV
Water pump Water Valve
Heating circuit

## Slide 9
Focusing on laying out businesses such as key components of the thermal management system for new energy vehicles with internationally leading technologies.
A leading company in the global refrigeration accessories industry, the market share of stop valves ranks first in the world, four-way valves ranks second in the world, and electronic expansion valves ranks second in the world
One of the core suppliers with the most complete nuclear power HVAC products and the highest technical content
HVAC

## Slide 10: Parts and components - covering the whole field of refrigeration and AC
Heat exchanger product line
Thermal management product line
壳管
微通道
Refrigeration component product line
Electronic expansion valves ranks second in the world
The market share of stop valves, small pressure vessels, and system integrated piping components ranks first in the world
The four-way valve ranks second in the world
EEV
Four-way valve
Shut-off valves
Small containers
Tube assembly
Other parts
Fins
Microchannels
Shell tubes
Automotive thermal management

## Slide 11: Business layout - global marketing
店口
杭州
DunAn America
European Company (Germany）
Japanese company
Korean company
India Office
Malaysia Office
Thai company
Mexico
DunAn Headquarters
Overseas companies/marketing agencies
R&D center
Overseas companies or sales agencies in North America, Europe, Japan, South Korea, Thailand, India, Malaysia and other locations;
Overseas marketing layout:

## Slide 12: DunAn Vehicle Thermal Management - Preferred supplier of thermal management components
Expansion valve series
Small diameter EXV
Large diameter MFEV
R744 EXV
SO-TXV
Solenoid valve, check valve series
Water pumps
Water valve series
SOV series (06/12/16）
CV series (10/12/16)
EP60series (37~120W)
EP70series (80~120W)
EP80Series (170~250W)
Multi-way disc valve series
Multi-way column valve series
Three-way proportional control valve series

## Slide 13: Electronic expansion valves
By automatically adjusting the refrigerant flow, the system operation efficiency is improved, to achieve the goals of rapid cooling or heating, precise control, energy saving, etc. (The corresponding diameter products can be customized)
Test conditions: Inlet pressure 1.5 MPa, inlet subcooling 5°C, outlet pressure 0.2 MPa
Model | Diameter (mm) | Nominal capacity R134a (kW) | Maximum working pressure (MPa) | Maximum operating pressure difference (MPa)
MEV-1.0 | Φ1.0 | 3.5 | 4.2 | 3.5
MEV-1.65 | Φ1.65 | 6 |  | 
MEV-1.8 | Φ1.8 | 8 |  | 
MEV-2.0 | Φ2.0 | 9 |  | 
MEV-2.2 | Φ2.2 | 10 |  | 
MEV-2.6 | Φ2.6 | 13 | 3.5 | 2.1
MEV-3.2 | Φ3.2 | 22 |  | 
Applicable refrigerant | R134a、R1234yf
Maximum working pressure | 4.2MPa
Applicable ambient temperature | -40℃～120℃
Rated voltage | DC12V
Voltage range | DC 9V～16V
Number of full-on pulses | 500 pulses
Control method | LIN/PWM
Excitation method | 1~2 phase excitation
Service life | ≥ 200,000 times
Electronic Expansion Valve

## Slide 14: Electronic expansion valves
PWM-EXV
LIN - EXV (A)
LIN - EXV (B)
LIN - EXV (C)
Plug-in small diameter - EXV

## Slide 15: Electronic Expansion Valve Small Diameter EXV Low Internal Leakage Series
Adopt bearing structure;
1st generation
(existing products)
Bearing structure
Valve needle parts
Soft seal
2nd generation
(low internal leakage series)
Low internal leakage is ensured throughout the life cycle, which can be ≤20ml/min@1Mpa or even lower;
Adopt soft sealing valve port;
Relying on the existing structure to upgrade and optimize the design, the reliability is higher.
Product Advantages
Promotion progress
Already in mass production

## Slide 16: Electronic Expansion Valve Large Diameter Electronic Valve Series
FBEV (Parabolic)
Bearing Structure
Low internal leakage throughout the life cycle
Soft seal
Internal balance, bidirectional
MFEV (broken line)
Bidirectional throttling and full flow
High precision, small flow, throttling
Low internal leakage throughout the life cycle
High reliability
Three-way electronic valve TWEV
One inlet, two outlets
High-precision refrigerant distribution
Can throttle, pressure adjustment, and stop the flow.
Outlet 1
Outlet 2
Inlet

## Slide 17: Electronic Expansion Valve Large Diameter FBEV Single Valve Needle Series
FBEV (Parabolic)
Adopt internal balance and bearing structure, higher operating life and reliability;
Adopt soft sealing valve port, low internal leakage in the whole life cycle, 100ml/min @1Mpa;
It can be expanded to 16 diameter to meet the needs of lower flow resistance, no solenoid valve switching noise, smooth switching to reduce the impact of switching on the system;
Product Advantages
Promotion progress
Mass production parts
Parabolic
Air flow Q
Pulse numbers P

## Slide 18: Thermal Management System Heat Pump System Application Scenarios Loop Refrigerant Distribution
Application of refrigerant distribution in different loops
Condenser 1
Condenser 2
Gas

## Slide 19: Thermal Management System Heat Pump System Application Scenario Battery Direct Cooling Pressure Regulation
Direct cooling plate temperature uniformity requirement, pressure regulation at the same time
Compressor
External Exchange
Battery direct cooling plate

## Slide 20: (Solenoid) thermal expansion valve series
Conventional type - TXV
Normally closed type - SOTXV
Normally open type - SOTXV

## Slide 21: Solenoid valves
CDF-10 (Special-shaped forgings)
CDF-06（Square）
CDF-06 (Threaded interfaces)
CSF-10 (10 Three-way solenoid valve)
CDF-16D (Special-shaped forgings)
Cartridge solenoid valve 12D
Cartridge solenoid valve 12D - 2nd generation
Cartridge solenoid valve 16D
Cartridge solenoid valve 16D - 2nd generation

## Slide 22: Check valves
Flow resistance test conditions: Inlet pressure 1.5Mpa, inlet superheat 20°C, refrigerant flow rate 150 kg/h
Model | Diameter（mm） | Flow resistance | Maximum operating pressure (MPa） | Open Differential Pressure at Open State (KPa） | Internal leakage (ml/min）
MCV-10-001 | Φ10 | ＜10 | 3.5 | ≤10 | ≤20
MCV-16-001 | Φ16 | ＜5 | 3.5 | ≤5 | ≤20
Item | Parameters
Applicable media | R134a、R1234yf
Maximum working differential pressure | 3.5MPa
Valve opening pressure | ≤15KPa
Medium temperature | -40℃～+125℃
Humidity range | ＜95%RH
Service life | ≥200000 times
Directs the flow of refrigerant and prevents backflow

## Slide 23: Trends in NEV refrigerant valves

## Slide 24: Refrigerant Valve Trend 1: Low Cost (Compact, Lightweight)
The 2nd generation of 12mm compact cartridge solenoid valve
Project | Parameter
States | Normally Open / Closed
Diameter | φ12mm
Work pressure | 0 to 3.1MPa
MOPD | Normally open 2.5MPa Normally closed 2.1MPa@9VDC, 20°C
Applicable refrigerant | R134a、R1234yf PAG、POE
Medium temperature | -40℃～+120℃（HNBR）
Internal leakage | ＜30ml/min
Service life | ≥200,000 times
Rated voltage | DC12V
Low internal leakage
Compact
small size
Low flow resistance
Long life span
Features:
Reliable
High differential working pressure

## Slide 25: Product comparison | 12mm 1st generation VS 12mm 2nd generation
Product Specifications: | 12mm Second generation | 12mm
Applicable refrigerant | R134a、R1234yf | R134a、R1234yf
Internal Leakage | ＜30ml/min | ＜100ml/min
Differential working pressure | 0 to 2.1MPaNormally closed 0 to 2.5MPaNormally open | 0 to 1.5MPaNormally closed 0 to 2.5MPaNormally open
Work pressure | 0 to 3.1MPa | 0 to 3.1MPa
Endurance | 200,000+ | 150,000+
Operating voltage | 9 to 16VDC | 9 to 16VDC
Flow resistance | 6kpa | 8kpa
Weight | 160 | 182
12mm SOV 2nd generation is designed for thermal management integration；
The comprehensive performance has been improved;
Based on the update and iteration of existing batch products, the product has high reliability;
The 10&12mm solenoid valve has the smallest installation space on the market has a installation area reduced by more than 25% compared with similar solenoid valve products.
2nd generation
1st generation
Flow resistance test conditions: Inlet pressure 1.5Mpa, inlet superheat 20°C, refrigerant flow rate 150kg/h

## Slide 26: Comparison of installation dimensions
Compared with the 12mm SOV 1st generation, the installation size is 25%+ smaller, which can help make the size of the integrated component smaller, and further reduce the weight, volume and cost of the integrated component.

## Slide 27: The 2nd generation 16mm miniaturized SOV
Project | Parameter
States | Normally Closed
Diameter | φ16mm
Work pressure | 0 to 3.1MPa
Differential working pressure | 0 to 1.5MPa @9VDC，20℃
Applicable media | R134a、R1234yf PAG、POE
Medium temperature | -40℃ to 120℃（HNBR）
Internal leakage | ＜10ml/min
Service life | ≥ 150,000 times
Rated voltage | DC12V
Low Internal Leakage
Small size
Low cost
Low flow resistance
Features:
0 differential pressure valve opening
Light-weight

## Slide 28: Product comparison | 16mm 1st generation VS 16mm 2nd generation
Product Specifications: | 16mm Second generation | 16mm
Applicable media | R134a、R1234yf | R134a、R1234yf
Internal Leakage | ＜30ml/min | ＜100ml/min
Differential working pressure | 0to 1.5MPa | 0.007 to 1.5MPa
Work pressure | 0 to 3.1MPa | 0 to 3.1MPa
Endurance | 150,000+ | 150,000+
Operating voltage | 9 to 16VDC | 9 to 16VDC
Flow resistance | 19.6KPa | 19.9KPa
Weight | 161g | 251g
16mm SOV
2nd generation
16mm SOV generation
Note: The flow resistance condition is the inlet pressure of 0.23MPa, the superheat is 5K, and the flow rate is 150kg/h
The 16mm SOV 2nd generation is designed for thermal management integration.
The comprehensive performance has been improved;
The first-stage pilot mode is used to realize the opening of the 16 diameter solenoid valve;
The 16mm solenoid valve, which has the smallest installation space on the market, has a more than 50% installation area compared with similar solenoid valve products.

## Slide 29: Comparison of installation dimensions
Compared with the first generation of 16mm SOV, the installation size is more than 50% smaller!

## Slide 30: The 2nd-generation compact SOV integration Optimization comparison example
Before
After
97mm
81mm
H=44mm
84mm
65mm
H=42mm
134mm
119mm
Runner plates V≈275cm³
M=742.5g
Runner plates + SOV*3 M=1.303kg
Runner plates V≈245cm³
M=661g
Runner plates + SOV*3 M=1.126kg
The size of the runner plate is significantly reduced in the length and width direction, which is reduced by 15mm and 13mm respectively, the volume is reduced by 30cm³, the weight is reduced by 0.177kg, and the reduction is optimized by more than 10%.

## Slide 31: Refrigerant Valve Trend 2: Multi-function (Large-diameter Flow Distribution and Regulation)
Refrigerant distributing applications with different ways
The battery is directly cooled at the outlet for pressure regulation applications
Condenser 1
Condenser 2
External Exchange
Gas
Compressor
Battery direct cooling plate

## Slide 32: Refrigerant valve trend 2: Multi-Functional (MFEV)
Bearing structure
Inner equilibrium structure
Soft-seal valve port
MFEV
• The industry's first double-pin structure design, two-way throttling, full flow, and cut-off
• The throttling part of the flow can be customized, and there are currently three specifications of 5/7/10KW (equivalent to 1.3/1.65/2.2 diameter EXV throttling capacity)
• Low internal leakage (≤100ml/min), Low noise (≤35db)
• Stronger resistance to foreign body impurities.
Product Advantages:
Promotion
It has been mass-produced
At present, DunAn is the only manufacturer in China with mass production capacity

## Slide 33: Function introduction
Air flow curve：
Small valve needle throttle section
Large valve pin throttle section
EXV function
Single Valve needle FBEV function
SOV Full open function
Throttling state
Full statuoffs
Transmission screws
Large valve pin
Small valve pin
The large valve port is opened
The smallvalve port is opened
smallThe valve port is closed
The large valve port is closed
Full circulation
Compressor
Pulse numbers
Flow
Flow
Flow

## Slide 34: Introduction to typical application scenarios - Full circulation, throttling switchable function
Application: Mode switching, Outdoor Heat Exchanger (OHX)/Liquid Cooled Condenser (LCC) as a condenser in refrigeration mode and evaporator in heat pump mode.
Functional requirements: In refrigeration mode, the valve is fully flowing, and the pressure drop is close to 0, and in heat pump mode, the valve has a good throttling control function as an expansion valve.

## Slide 35: Introduction to typical application scenarios - Full circulation, throttling switchable function
SOV + Expansion
valve in parallel
MFEV
Functional Integration
For each single element, the technology is relatively mature; Expansion valves can meet the accuracy requirements required for throttling.
Large size and heavy weight; 2 actuators need to be controlled; In bypass mode, it is not adjustable.
Small size / weight; The cost advantage brought by the integrated design of single valve function; Take into account the functions of throttling and full circulation; The bypass mode is adjustable (to meet the requirements of efficient dehumidification).
Advantages
Shortcoming
VS
Advantages

## Slide 36: Refrigerant Valve Trend 2: Multi-function (Multi-way)
 | Project | Parameter
1 | Refrigerants | R134a,R1234yf
2 | MOPD | 2.5MPa
3 | Burst pressure | 21MPa
4 | Operating temperature | -40℃~+120℃
5 | Refrigerant temperature | -40℃~+120℃
6 | Rated voltage | DC12V
7 | Operating voltage | DC9~16V
8 | Work itinerary | 640 pulses
10 | Maximum circulation caliber | Φ12mm
11 | Control mode | PWM or LIN
12 | Internal leakage | ≤100mL/min
13 | Working life | ≥150,000 cycles
Three-way electronic valve (TWEV)
Outlet 1
Outlet 2
Inlet

## Slide 37: How it works
The internal balancing channel equalizes the pressure and reduces the actuation force required for the valve pin
The flow adjustment slope adjusts the angle according to customer needs to realize the flow resistance adjustment of A-B and A-C flow paths
B
C
A
The whole trip is mainly divided into the following 5 sections: 1. Ports A-B are fully open and ports A-C are closed; 2. Low flow resistance at port A-B and high flow resistance at port A-C, to achieve flow regulation in the small flow section of port A-C; 3. Low flow resistance at A-B port and low flow resistance at A-C port to achieve A-B and A-C low flow resistance operation at the same time, and the actual flow ratio is determined by the pipeline and heat exchanger of the two branches; 4. High flow resistance at port A-B, low flow resistance at port A-C, flow regulation in small flow section of port A-B is realized; 5. Ports A-B are closed, and ports A-C are fully open;
Interval 1
Interval 2
Interval 3
Interval 4
Interval 5
Total Flow

## Slide 38: TWEV Application scenarios
1、Three-way proportional adjustment function - real-time dynamic distribution of refrigerant
2、Three-way switching function - refrigerant circuit switching
Condenser WCC, etc.
Battery direct cooling plate
Compressor

## Slide 39: Refrigerant Valve Trend 2: Multi-Functional (MFEV)
 | Item | Parameters
1 | Refrigerants | R134a,R1234yf
2 | Use pressure | 0~4.2MPa
3 | Burst pressure | 21MPa
4 | Operating temperature | -40℃~+120℃
5 | Refrigerant temperature | -40℃~+120℃
6 | Rated voltage | DC12V
7 | Operating voltage | DC8~16V
8 | Number of pulses in the full stroke | 640 pulses
9 | MOPD | 2.5MPa（9V）
10 | System switchover time | 5~15S
11 | Circulating caliber | Φ12mm
12 | Drive mode | PWM / LIN
13 | Internal leakage | ≤100mL/min（1MPa）
14 | Service life | ≥150,000 cycles
Combined Four-Way Valve（FWEV）

## Slide 40: How the product works
B
A
C
b
c
a

## Slide 41: How the product works
Principle: The system switching function is realized in the form of a combination of two three-way valves. The action is initiated by the electronic three-way valve, and after the electronic three-way valve completes the switching, the mechanical three-way switching valve automatically switches with the change of system pressure.
A
B
C
a
c
b
A
B
C
a
c
b
Electronic 3-way valve
Compressor
Outdoor heat exchanger
3-way switching valve
EXV
Indoor heat exchanger
Outdoor heat exchanger
Electronic 3-way valve
Compressor
3-way switching valve
Indoor heat exchanger
EXV
Cooling mode
Heating mode

## Slide 42: Refrigerant Valve Trend 2: Multi-Functional (MFEV)
Electronic expansion valve for car refrigerators
No. | Project | Parameter
1 | Refrigerants | R134a、R1234yf and its corresponding POE
2 | MOPD | 2.5MPa
3 | Maximum operating pressure | 3.5MPa
4 | Refrigerant temperature | -40℃～+125℃
5 | Rated voltage | DC12V
6 | Operating voltage | DC9～16V
7 | Maximum circulation diameter | Φ0.8mm
8 | Control mode | PWM or LIN
9 | Internal leakage (bi-directional shut-off) | 1.0MPaThe amount of air pressure leakage≤300ml/min
10 | life span | ≥100，000 cycles
11 | Rated cooling capacity | 0.75KW

## Slide 43: EXV for car refrigerator - refrigeration capacity, air flow curve
Refrigeration capacity test data
Note: Below 150 pulses, the flow rate is too small, the test equipment is limited, and the data is not measured；
Test items and results
Sample medium
Tester
Yang Jinghua
Testing location
R32 Capacity Table
Test conditions
Test results
Serial No.
Flow direction
Pulse
Pressure
before valve
Temperature
before valve
Subcooling
Pressure
after valve
Refrigerant flow
Cooling capacity
(Steps)
Note: The pressure before the No. 5 EXV is 1500 kPa, the pressure after the valve is 300 kPa, and the subcooling degree is 5°C. The pressure before the valve and the pressure after the valve are absolute pressures.

## Slide 44: EXV for car refrigerator - refrigeration capacity, air flow curve
Refrigeration capacity:
Rated cooling capacity: 0.75KW；
Fully open 576 pulse cooling capacity: less than 0.9KW;
Air Flow:
100 Pulsed air flow：1 L/min@0.1MPa
576 Pulsed air flow： 4 L/min@0.1MPa
Flow curve
Pulses

## Slide 45: Refrigerant Valve Trend 3: High Performance & Low Noise
Noise-reducing structure EXV--It can be applied to the refrigeration condition without subcooling to solve the problem of refrigerant noise
Sound attenuating filter1
Sound attenuating filter2
Connecting sleeve
Plug-like flow area (Discontinuous large bubbles)
Bubble flow area (continuous small bubbles)
Bubbles after refinement
Discontinuous large bubbles

## Slide 46: Refrigerant Valve Trend 3: High Performance & Low Noise
Benefits: To solve the problem of fluid noise of gas-liquid two-phase refrigerant flowing through the valve body without subcooling in front of the valve under refrigeration conditions, our company eliminates the sound of discontinuous air flow by setting up a double-layer silencing filter structure in front of the refrigeration valve.
Customer promotion progress：
***The project has been mass-produced, which has completely solved the previous noise problem;

## Slide 47: 16mm diameter Silent Series Solenoid Valve
Existing designs
Optimized design
Please check next slide for details

## Slide 48: 16mm diameter Silent Series Solenoid Valve
Operating noise less than 45db@50cm (65db or more for existing products)
Add a patented noise reduction mechanism: it does not work at the moment of opening the valve, does not reduce the suction force of the core iron, and can be buffered to reduce noise when it is sucked;
The new design is adopted, so that the core iron stroke is irrelevant to the piston stroke, and the impact force of the engagement is minimized;
The normally closed solenoid valve can be reversed to support the normal flow function
The unique piston structure design solves the problem that the original structure cannot be reversed.
Core iron opening
Vibration damping pads

## Slide 49: Silent series solenoid valve
The sample was tested in the system for noise, and the test results are as follows:
Noise level:
Suction noise：41.8 dB
Valve shut-off noise：43.2 dB

## Slide 50: Refrigerant Valve Trend 3: High Performance (Low Internal Leakage)
EXV Low internal leakage series
1st Generation (Existing Products)
2nd Generation (Low Leakage Series)
Product Advantages:：
Bearing structure is adopted；
Low leakage throughout the life cycle ensures that it can achieve ≤ 20ml/min@1Mpa or even lower；
Soft-seal valve port is used；
Relying on the existing structure to upgrade and optimize the design, the reliability is higher.
Client Promotion：
*** project has been mass-produced。
Soft gaskets
Bearing structure pin parts

## Slide 51: Refrigerant Valve Trend 3: High Performance (Low Internal Leakage)
Low internal leakage and large diameter series -- Low internal leakage capacity of the leakage grade
No. | Item | Parameter
1 | Refrigerants | R134a,R1234yfand the corresponding POE oil
2 | MOPD | 1MPa
3 | Maximum operating pressure | 3.1MPa
4 | Refrigerant temperature | -40℃~+105℃
5 | Rated voltage | DC12V
6 | Operating voltage | DC9~16V
7 | Maximum circulation caliber | Φ16mm
8 | Control mode | PWM or LIN
9 | Internal leakage (bi-directional shut-off) | Positive: Refrigerant leakage400g/y@2.4MPa or Helium leakage He检2.1e-3mbar.l/s@2.4MPa Reverse: refrigerant leakage rate 400g/y@1MPa or Helium leakage He检2.1e-3mbar.l/s@1MPa
10 | life span | ≥150,000 cycles

## Slide 52: Refrigerant Valve Trend 3: High Performance (Low Internal Leakage)
Product Advantages:：
Reliable low leakage， Helium leakage He检2.1e-3mbar.l/s@2.4MPa；
High life, high reliability，Helium leakage ≥150,000 cycles。
Client Promotion：
***New project has been negotiated；
Cone valve port, long life, reliable.
Low internal leakage and large diameter series

## Slide 53: Brief summary

## Slide 54: Contact Info
Thank you
      Victor Zhang
      DunAn Vehicle Thermal Management Co., Ltd.
      Intelligent Vision Industrial Park, No.9 Xingnong Road, Zhuji City, Zhejiang Province, China
      (+1) 5127742988
      zhangsc@dunan.cn