## Slide 1
Prepared for
2025 Thermal Management Symposium
Tanguy Cabaret
Ypsilanti, October 14-15, 2025
Development of TMS
for BEV and FCEV trucks

## Slide 2
Thermal Management system
BEV
Thermal Management system
FCEV

## Slide 3
Thermal Management system
BEV
Thermal Management system
FCEV

## Slide 4: Commercial vehicles’ TMS is divided in 4 main sub-systems with specific requirements: battery, EDU & PE, cabin and brake resistors
CV TMS – SUB-system overview
EDU: electric drive unit; PE: power electronics Source: FEV
BATTERY THERMAL MANAGEMENT SYSTEM (BTMS)
CABIN THERMAL MANAGEMENT SYSTEM
BRAKE RESISTORS THERMAL MANAGEMENT SYSTEM
EDU AND PE THERMAL MANAGEMENT SYSTEM
4 main sub-systems compose CV thermal management system

## Slide 5: Lower level of integration between the different thermal management systems is currently observed in the CV segment compared to PVs
CV: commercial vehicle; PV: passenger vehicle; EDU: electric drive unit; PE: power electronics Source: FEV
BATTERY THERMAL MANAGEMENT SYSTEM (BTMS)
CABIN THERMAL MANAGEMENT SYSTEM
BRAKE RESISTORS THERMAL MANAGEMENT SYSTEM
EDU AND PE THERMAL MANAGEMENT SYSTEM
Currently lower integration and interactions observed between the different TMS in CVs compared to PVs
CV TMS – SUB-system overview

## Slide 6: The current low level of TMS integration for CVs can be explained by factors linked both to market conditions and technological challenges
CV: commercial vehicle; PV: passenger vehicle; EDU: electric drive unit; ICE: internal combustion engine Source: FEV
BATTERY THERMAL MANAGEMENT SYSTEM (BTMS)
CABIN THERMAL MANAGEMENT SYSTEM
BRAKE RESISTORS THERMAL MANAGEMENT SYSTEM
EDU AND PE THERMAL MANAGEMENT SYSTEM
Currently lower integration and interactions observed between the different TMS in CVs compared to PVs
CV TMS – SUB-system overview
Technological challenges and low maturity
Market conditions and internal OEM organization
2 main reasons explain the lower level of integration of CVs TMS compared to PVs
Multiple suppliers' sub-systems integration
Internal OEM organization
Electrification skepticism
Commercial vehicle specific component availability
Technology maturity and reliability
Low commercial vehicle xEVs sales volumes
Specific cooling requirements

## Slide 7: Commercial vehicle TMS layouts are differentiated by 4 main factors that are impacting the design and the efficiency of the system
CV TMS – MAIN DESIGN DIFFERENTIATION FACTORS
Source: FEV
Refrigerant circuit(s) integration
EDU and PE integration
Heat pump adoption
Brake resistors cooling
Main current approaches
Main challenges
  High battery cooling requirements
  limited power of AC compressor
  Separate refrigerant circuits for battery and cabin cooling as main solution
  High cooling need of EDU and PE
  Single circuit for PE and EDU in most CVs, but diversity of solutions remain
  High costs of development and integration
  Only visible for LCVs today
  High heat energy to dissipate
  Risk to overheat other comp.
  Need to oversize some components (e.g., electric fan)
  Dedicated coolant circuit or integration with battery loop

## Slide 8
Thermal Management system
BEV
Thermal Management system
FCEV

## Slide 9: Fuel cell vehicles can be clustered in range-extender, mid-power and full-hybrid depending on the relevance ratio between fuel cell and battery
Fuel cell powertrain CLUSTERING
Source: FEV
MID-POWER FCEV
+
REFCEV
FULL-HYBRID FCEV
+
+
Primary source of power
Range extender
More common on LCV segment
Balanced power between fuel cell and battery
Past & current state-of-the-art on M&HD
Primary source of power
Additional power and regen. braking
Current & future M&HD

## Slide 10: Lower level of integration between the different thermal management systems is currently observed in the CV segment compared to PVs
CV: commercial vehicle; PV: passenger vehicle; EDU: electric drive unit; PE: power electronics Source: FEV
CABIN THERMAL MANAGEMENT SYSTEM
CV TMS – SUB-system overview
BATTERY THERMAL MANAGEMENT SYSTEM (BTMS)
EDU AND PE THERMAL MANAGEMENT SYSTEM
BRAKE RESISTORS THERMAL MANAGEMENT SYSTEM
Possible leveraging of thermal architecture from BEV or ICE, with adaptation to FCEV powertrain
FUEL CELL THERMAL MANAGEMENT SYSTEM
H2
O2

## Slide 11: Integration of several BoP components with TMS system enables to ensure optimal temperature and water management in the fuel cell system
FCEV TMS – BOP integration
Source: FEV
Why
What
How
Are BoP components integ. within TMS ?
Temperature management
Water management
FC air compressor
H2 recirculation blower / pump
H2 heater
Intercooler
Anode water separator
FC related PE (e.g., DC/DC boost,)
Integration with LT/MT coolant loop
Integration with fuel cell HT coolant loop
components can be integrated with TMS ?
are the BoP components integ. with TMS ?
Main integ. reason
Possible integ. reason
Rarely integ. with TMS
Sometimes integ. with TMS
Often integ. with TMS
Main observed integration
Other observed integration

## Slide 12: Fuel cell thermal management system complexity increases compared to BEV one, due to additional components and cooling efforts
BEV TMS
FCEV TMS
BEV VS FCEV vehicles Thermal architectures
FC: fuel cell; EDU: electric drive unit; PE: power electronics; PV: passenger vehicle; MD: medium duty; HD: heavy duty; PTC: positive temperature coefficient Source: FEV
Thermal loops
PE and EDU cooling
Cabin management
Current integration level
Battery cooling
Qualitative assessment
Coolant
Controls and complexity
3 to 4 loops
+
4 to 5 loops
Dedicated LT + refrigerant
Dedicated LT + refrigerant Refrigerant only possible
MT loop – coolant or oil for EDU
Additional FC auxiliaries
PTC/HP for heating
possible heat re-use
Limited on CV – high on PV
Low, including for PV
No major challenge
Low electric conductivity, material compatibility
Battery TMS as major challenge
Battery and fuel cell TMS
Complexity

## Slide 13: TMS development trends are divided into performance, integration and sustainability considerations; multiple factors to take into account
PERFORMANCE
Cooling / heating / efficiency / functionality optimization
INTEGRATION
Complexity and cost reduction, portfolio synergies
SUSTAINABILITY
Environmental and safety compliance
Multiple int. or ext. influence factors
Powertrain components trends
Global make-or-buy strategy
Regulatory framework
and more…
TMS
global trends
TMS TRENDS - INTRODUCTION
Source: FEV

## Slide 14: Efficiency level is mainly determined through heat exchanges and re-use possibilities, while integration is defined by the level of TMS centralization
TMs clustering – EXPLANATION
Source: FEV
Exemplary ranking criteria
Exemplary ranking criteria
Presence of a heat pump
Integration of multiple EDUs
Advanced heat exchange possibilities (e.g., chillers, LCCs)
Merge of EDU and PE circuits
Centralized thermal management module
Integration of brake resistor circuits with others
Re-use of waste heat
Limited utilization of PTC heaters
Utilization of multi-way valves
Merge of cabin and battery refrigerant circuits
…
…
Integration level
No
Partially
Highly
Number or functions & Efficiency level
Basic
Intermediate
Advanced

## Slide 15: Current PV thermal management systems are both more integrated and more efficient than M&HD ones, especially through adoption of ITMS
TMs clustering – PV VS M&HD comparison
CIM: coolant integrated module; RIM: refrigerant integrated module; ITMS: integrated thermal management module Source: FEV
No
Partially
Highly
Share of available CV BEV models
Share of available PV BEV models
Integration level
No
Partially
Highly
Number or functions & Efficiency level
Basic
Intermediate
Advanced

## Slide 16: M&HDs are expected to reach an intermediate to advanced TMS performance by 2030, and partial to high level of integration by 2035
TMs TRENDS – 2030 and 2035 development path
Source: FEV
Integration level
No
Partially
Highly
Functionality & Efficiency level
Basic
Intermediate
Advanced
Current M&HD situation
  Integration
  No to partial integration through sub-modules (e.g., HVAC, battery)
  Performance
  Basic to intermediate performance (e.g., re-use of waste heat)

## Slide 17: M&HDs are expected to reach an intermediate to advanced TMS performance by 2030, and partial to high level of integration by 2035
TMs TRENDS – 2030 and 2035 development path
Source: FEV
Integration level
No
Partially
Highly
Functionality & Efficiency level
Basic
Intermediate
Advanced
  Integration
  Low focus towards 2030
  Mainly sub-modules
  Performance
  Intermediate to advanced to improve efficiency
  E.g., heat pump, improved HEX, HV components
Current M&HD situation
2030 focus

## Slide 18: M&HDs are expected to reach an intermediate to advanced TMS performance by 2030, and partial to high level of integration by 2035
TMs TRENDS – 2030 and 2035 development path
Source: FEV
Integration level
No
Partially
Highly
Functionality & Efficiency level
Basic
Intermediate
Advanced
  Integration
  Larger development of semi- integrated modules
  CV dedicated fully integrated modules for premium OEMs
  Not expected to be as integrated as PVs ITMS
  Performance
  Continuous improvements to reach advanced levels
2030 focus
Current M&HD situation
2035 focus

## Slide 19
Contact Details
FEV Consulting Inc.
444 N Michigan Avenue
Chicago, Il, 60611
consulting@fev.com
www.fev-consulting.com
Tanguy Cabaret
Consultant
FEV CONSULTING
+1 248 739 2611
cabaret@fev.com