## Slide 2: Modeling of Thermal Runaway Propagation in Battery Module Considering Vent Gas Combustion
Haechan Choi, Hyunjoo Kim, Kyoungdoug Min*

## Slide 3: Introduction
Characteristics of thermal runaway
Positive temperature feedback loop : Hotter battery generate more heat due to chain chemical reactions
Large amount of heat generation : Highly reactive internal chemicals generate sufficient heat to raise the battery temperature above 1000 °C.
Generation and release of vent gas : Release of large amounts of high-temperature gas mixed with flammable gases and oxygen
Integrated modeling incorporating all 3 elements is required
 Detailed incorporation of chemical reactions is essential.

## Slide 4: Introduction
Volatile chemicals inside the battery are highly sensitive to temperature changes.
Various chemical reactions occur simultaneously inside the battery during thermal runaway.
Complex chain reactions make it difficult to understand thermal runaway kinetics.
The exact mechanism remains unidentified due to complex reactions in a confined area.
Chemical reactions during thermal runaway
Anode region
Cathode region
Electrolyte region
Self decomposition of SEI
SEI + Li
SEI + Fluorinated gases
Li + Binder (CMC)
Polymerization of Electrolyte
Decomposition of Salt
Oxidation of Electrolyte
Salt + Electrolyte
Salt + moisture
Phase transition of cathode
Binder + Li
Oxidation of conductor carbon
Transport of chemical species

## Slide 5: Introduction
Hydrocarbons (CH4, C2H4, C2H6, etc.)
Oxygen
Hydrogen, water
Carbon dioxide, carbon monoxide
Reported chemical reactions
Others (PF5, POF3, etc.)
Generation of flammable gases and oxygen through chemical reactions
Ignition due to heat generation or arc formation between electrodes
 Combustion of vent gas

## Slide 6
Composition of vent gas (Graphite/NMC811 pouch cell)
[Wang et al., Journal of Power Sources, 2024.]
[Zou et al., International Journal of Heat and Mass Transfer, 2022.]
[Chen et al., Journal of Loss Prevention in the Process Industries, 2020.]
Main components of vent gas include CO₂, CO, H₂, and hydrocarbons.
Experimental conditions can lead to varying results even for batteries with the same chemistry.
Contrary to chemical predictions, O₂ and H₂O are not detected.
Introduction

## Slide 7: Objective
Analysis of the effect of vent gas combustion on thermal runaway propagation using CFD simulation in a battery module
Contents
Development of a thermal runaway model capable of predicting vent gas composition
Development of a CFD simulation for thermal runaway propagation within a battery module
Analysis of thermal runaway propagation mechanisms within the battery module

## Slide 8: Models used in research
Heat generation model
Model for simulating heat generation as a function of battery temperature
3 equations for anode, 3 equations for cathode, 1 equations for electrolyte
Chemical reaction model
Model for calculating quantity & composition of vent gas
Coupling chemical reactions with the heat generation model to determine reaction extent
Considering a total of 8 chemical reactions
Simulation for thermal runaway propagation
Simulation for modeling and analyzing thermal runaway propagation within the battery module
Developed using the commercial CFD tool STAR-CCM+

## Slide 9: Schematic of research framework
CFD simulation for TRP
Heat generation model
Chemical reaction model
(T: temperature, : heat generation rate, : conversion rate, : mass flow rate of vent gas, : Composition of vent gas)
Reaction rate:
Heat generation rate:
(α: conversion ratio, : frequency factor, : reaction order, : Activation energy, : Enthalpy of reaction)
Reaction:
(: molar amount of species, : initial molar amount of species)
Calculation of conjugate heat transfer
Heat transfer between cell & air
Heat transfer between cell & plate
Modeling of vent gas combustion
Use of chemical kinetic mechanism
Calculation of heat generation from reactions
Tracking of air composition within the module
TRP: Thermal runaway propagation

## Slide 10: Methodology (Heat generation model)
Decomposition rate
(, )
Heat generation rate
Anode
Electrolyte
Separator
SEI
Cathode
 3 reactions, kinetic parameters from Ren et al.
 3 reactions, kinetic parameters from Wang et al.
 1 reactions, kinetic parameters from Kim et al.

## Slide 11: Methodology (Chemical reaction model)
Anode reaction | p-SEI decomposition | (CH2OCO2Li)2  Li2CO3 + C2H4 + CO2 + 0.5O2
 | s-SEI regeneration | 2Li + 2C3H4O3  (CH2OCO2Li)2 + C2H4
 | s-SEI decomposition | Li2CO3 + PF5  2LiF + POF3 + CO2
 | CMC decomposition | CMC-OH + Li  CMC-OLi + 0.5H2
Cathode reaction | Structural collapse (Layered  Spinel) | Li0.2MO2  0.4[Li0.5MO4] + 0.2O2
 | Structural collapse (Spinel  Rock salt) | 0.4[Li0.5MO4]  Li0.2MO1.2 + 0.2O2
 | PVDF decomposition | -CH2-CF2- + Li  LiF + -CH=CF- + 0.5H2
Electrolyte reaction | EMC evaporation | Liquid phase  Gas phase
Selection of chemical reactions suitable for NMC 811-based pouch cell through literature review

## Slide 12: Methodology (Chemical reaction model)
Coupling decomposition rate () with chemical reactions
Selected chemical reaction
Heat generation model
Chemical reaction model
Anode reaction 1 | p-SEI decomposition
 | s-SEI regeneration
Anode reaction 2 | s-SEI decomposition
Anode reaction 3 | CMC decomposition
Cathode reaction 1 | Structural collapse (Layered  Spinel)
Cathode reaction 2 | Structural collapse (Spinel  Rock salt)
Cathode reaction 3 | PVDF decomposition
Electrolyte reaction | EMC evaporation

## Slide 13: CFD Simulation setting
Cell
Plate
Insulating pad
Cell #6
Air
Exhaust hole
Part | Size [mm]
Cell | 340 x 11.5 x 100
Insulating pad | 340 x 6.2 x 100
Plate | 340 x 144.2 x 5
Exhaust hole | 144.2 x 20
Module | 350 x 144.2 x 103
Exhaust hole
Property | Value
Capacity | 60 Ah
Chemistry | Graphite / NCM811
Composition of electrolyte | 1:1 weight ratio of EC, EMC
Size of module components
Properties of battery cell

## Slide 14: CFD Simulation setting
Part | Number of mesh elements
Cell (each) | 40,005
Module | 180,290
Air | 544,782
- CFD tool: STAR-CCM+
- Time step: 0.001 - 1 sec (variable time step)
- Mesher: polyhedral
- Basic mesh size : 2 mm
- Number of mesh element

## Slide 15: CFD Simulation setting
Property | Value
Density | 2175 kg/m3
Specific heat | 1220 J/kg∙K
Thermal conductivity | 22.6 W/m∙K (in plane) 1.6 W/m∙K (through plane)
Thermal property of battery cell
[Li et al., Journal of Energy Storage, 2024]
Initial condition
Temperature of module : 300K
Temperature of cell #6 : 370K
Composition of air  N2:O2 = 0.78:0.22 (mole fraction)
Pressure of air : 1atm
Boundary condition
Exhaust hole – pressure outlet
Outer surface of air – adiabatic condition
Trigger for thermal runaway
Heat addition to cell 6 : 5000 W (Until 470 K)
Species | C2H4 | CO2 | O2
Mole fraction | 0.228 | 0.171 | 0.602
Vent gas ejection
Vent duration: 10 s
Mass flow rate: 0.00714 kg/s
Mole fraction

## Slide 16: Validation of heat generation model
Parameter | Exp. | Model
T1 (℃) | 91.3 | 88.1
T2 (℃) | 202.1 | 223.0
T3 (℃) | 745 | 755.9
Thermal characteristic parameters
- T1: Self-heating onset temp.
- T2: Thermal runaway occurred temp.
- T3: Maximum temp.
T1
T2
T3
[Zhang et al., Journal of Electrochemical Energy Conversion and Storage, 2023]
Comparison with experimental results of Zhang et al.
Comparison conducted between EV-ARC experimental results and modeling
Small difference in characteristic parameters
Futher improvement possible by incorporating endothermic reaction of the separator and internal short circuit reactions
Considered sufficiently reasonable for use in CFD

## Slide 17: Validation of Chemical reaction model
Comparison of experimental vent gas composition with modeling to validate the selected chemical reactions
Calculations using Cantera were conducted to reflect composition changes due to gas-phase reactions.
Chemical reaction calculations using Cantera are not included in the CFD simulation process.
Initial vent gas composition from chemical reaction model  Gas-phase reaction calculation using Cantera  Comparison
Validation process
A lithium-ion battery electrolyte surrogate model was used for the Cantera calculations.
This mechanism includes the combustion of lithium-ion battery electrolytes(EC, EMC, DMC and DEC).
The mechanism was numerically validated and calibrated using experimental data.
The calculations were performed under the assumption of isothermal and isobaric conditions.
Chemical reaction calculation
[Kanayama et al., Combustion and Flame, 2024]

## Slide 18: Validation of Chemical reaction model
Reaction calculations between gases using Cantera
Chart: 
| H2 | EMC | O2 | CO2 | C2H4 | POF3
 | 0.0002164 | 0.4235 | 1.8836 | 0.4778 | 0.6379 | 0.08703
POF3
EMC(g)
CO2
C2H4
O2
H2
Gas generation calculated through a chemical reaction model coupled with a heat generation model
Reactions between gases not considered
Rapid consumption of O2 and C2H4 through reaction
Absence of H₂ generation, unlike experimental results
Gas generation calculated through the chemical reaction model
POF3
EMC(g)
CO2
C2H4
O2
H2
Gas composition ratio

## Slide 19: Validation of Chemical reaction model
Temperature: 872.9℃
Amount of Gas Species (mol)
H2 | EMC | O2 | CO2 | C2H4 | POF3
0.0002164 | 0.4235 | 1.8836 | 0.4778 | 0.6379 | 0.08703
Gas Composition (mol)
Time | H2 | H2O | CO | CO2 | O2 | CH4 | Others
1 ms | 0.00294 | 0.00937 | 0.00777 | 0.2100 | 0.4198 | 0.00069 | 0.3494
1 s | 0.1043 | 0.3148 | 0.3265 | 0.2027 | 3.85E-06 | 0.03035 | 0.02129
1 min | 0.1465 | 0.2598 | 0.2820 | 0.2540 | 1.81E-16 | 0.04747 | 0.01022
1 hr | 0.1704 | 0.2243 | 0.2553 | 0.2865 | 2.28E-17 | 0.06319 | 2.66E-4
Time | H2 | H2O | CO | CO2 | O2 | CH4 | Others
1 ms | 0.00294 | 0.00937 | 0.00777 | 0.2100 | 0.4198 | 0.00069 | 0.3494
1 s | 0.1043 | 0.3148 | 0.3265 | 0.2027 | 3.85E-06 | 0.03035 | 0.02129
1 min | 0.1465 | 0.2598 | 0.2820 | 0.2540 | 1.81E-16 | 0.04747 | 0.01022
1 hr | 0.1704 | 0.2243 | 0.2553 | 0.2865 | 2.28E-17 | 0.06319 | 2.66E-4
Initial state of gases
1 min after
H2 | H2O | CO | CO2 | CH4
0.1465 | 0.2598 | 0.2820 | 0.2540 | 0.04747
Heat of reaction: 631.67 kJ
Amount of Gas Species (mol)
Arbitrary setting of reaction time to 1 min
H2, H2O, CO, CO2 ↑
O2, Other gas ↓
Significant variation in gas composition when inter-gas reactions are considered

## Slide 20: Validation of Chemical reaction model
[Yang et al., Applied Thermal Engineering, 2024] [Wang et al., Journal of Power Sources, 2024]
Chart: Vent Gas Composition(%)
| H2 | CO | CO2 | CH4 | O2 | Others
Experiment | 21.2 | 27.7 | 30.8 | 6.1 | 0 | 14.3
Model | 17.7 | 34.1 | 30.7 | 5.7 | 0 | 11.8
Previous research | 0.81 | 42.1 | 37.9 | 1.62 | 11.7 | 5.99
H2 CO CO2 CH4 O2 Others
High prediction accuracy of gas composition with a maximum deviation below 6.4%
Improved gas composition prediction compared to previous researches
 Demonstration of the validity of gas prediction using the chemical reaction model
 | Model | Previous research
H2 | - 3.5 | - 20.39
CO | + 6.4 | + 14.4
CO2 | - 0.1 | + 7.1
CH4 | - 0.4 | - 4.48
O2 | - | + 11.7
Others | - 2.5 | - 8.31
Difference with experiment

## Slide 21: Results
Time | Cell 1 | Cell 2 | Cell 3 | Cell 4 | Cell 5 | Cell 6 | Cell 7 | Cell 8 | Cell 9 | Cell 10 | Cell 11 | Cell 12
0 s | 300 | 300 | 300 | 300 | 300 | 370 | 300 | 300 | 300 | 300 | 300 | 300
90 s | 317 | 318 | 322 | 334 | 497 | 854 | 333 | 324 | 320 | 316 | 314 | 312
Cell 6 reaches its max. temp. (1037.6 K) at 62.2 s.
The other cells reach their max. temp. at 90 s.
At 90 sec, only Cell 4 exceeds 400 K, which is high enough to intiate thermal runaway
Due to the combustion of vent gas, the temp. of other cells also increased but remain below the self-heating temp.
Temperature of battery (at 0, 90 sec)

## Slide 22: Results
Cell
③
 | Cell 1 | Cell 2 | Cell 3 | Cell 4 | Cell 5 | Cell 7 | Cell 8 | Cell 9 | Cell 10 | Cell 11 | Cell 12
① | 259 | 264 | 312 | 8594 | 194484 | 2866 | 416 | 169 | 128 | 99 | 284
② | 7325 | 8644 | 11542 | 16086 | -1609 | 19123 | 12673 | 8608 | 5975 | 4430 | 3686
③ | 8914 | 9608 | 10203 | 10037 | 10208 | 11928 | 11094 | 11008 | 10238 | 8983 | 7610
Amount of heat transfer by path
(Unit: J)
3 Heat transfer mechanism
① Conduction heat transfer (direct) : Heat transfer through direct surface contact between cells
② Conduction heat transfer (via plate) : Heat transfer through the aluminum bottom plate
③ Convection heat transfer : Heat transfer through high temperature vent gas
Cell
①
②

## Slide 23: Results
Cell
 | Cell 1 | Cell 2 | Cell 3 | Cell 4 | Cell 5 | Cell 7 | Cell 8 | Cell 9 | Cell 10 | Cell 11 | Cell 12
① | 259 | 264 | 312 | 8594 | 194484 | 2866 | 416 | 169 | 128 | 99 | 284
② | 7325 | 8644 | 11542 | 16086 | -1609 | 19123 | 12673 | 8608 | 5975 | 4430 | 3686
③ | 8914 | 9608 | 10203 | 10037 | 10208 | 11928 | 11094 | 11008 | 10238 | 8983 | 7610
Amount of heat transfer by path
(Unit: J)
3 Heat transfer mechanism
① Conduction heat transfer (direct) : Heat transfer through direct surface contact between cells
② Conduction heat transfer (via plate) ③ Convection heat transfer
Cell
①
Direct conduction via surface contact accounts for 50.2 % of the total heat transfer.
Most of the heat transfer is concentrated in the adjacent Cell 5.
It’s the main cause of chain thermal runaway propagation in the module.

## Slide 24: Results
Cell
 | Cell 1 | Cell 2 | Cell 3 | Cell 4 | Cell 5 | Cell 7 | Cell 8 | Cell 9 | Cell 10 | Cell 11 | Cell 12
① | 259 | 264 | 312 | 8594 | 194484 | 2866 | 416 | 169 | 128 | 99 | 284
② | 7325 | 8644 | 11542 | 16086 | -1609 | 19123 | 12673 | 8608 | 5975 | 4430 | 3686
③ | 8914 | 9608 | 10203 | 10037 | 10208 | 11928 | 11094 | 11008 | 10238 | 8983 | 7610
Amount of heat transfer by path
(Unit: J)
3 Heat transfer mechanism
① Conduction heat transfer (direct)
② Conduction heat transfer (via plate) : Heat transfer through the aluminum bottom plate ③ Convection heat transfer
Cell
Conduction through plate below the module accounts for 23.3 % of the total heat transfer.
Cell 5 has a higher temp. than the plate, resulting in a negative heat transfer value.
Heat transfer through the plate tends to increase as proximity to Cell 6 increases.
②

## Slide 25: Results
Cell
 | Cell 1 | Cell 2 | Cell 3 | Cell 4 | Cell 5 | Cell 7 | Cell 8 | Cell 9 | Cell 10 | Cell 11 | Cell 12
① | 259 | 264 | 312 | 8594 | 194484 | 2866 | 416 | 169 | 128 | 99 | 284
② | 7325 | 8644 | 11542 | 16086 | -1609 | 19123 | 12673 | 8608 | 5975 | 4430 | 3686
③ | 8914 | 9608 | 10203 | 10037 | 10208 | 11928 | 11094 | 11008 | 10238 | 8983 | 7610
Amount of heat transfer by path
(Unit: J)
3 Heat transfer mechanism
① Conduction heat transfer (direct) ② Conduction heat transfer (via plate) ③ Convection heat transfer : Heat transfer through high temperature vent gas
Cell
Convection heat transfer accounts for 26.5 % of the total heat transfer.
Heat transfer by convection shows relatively more uniform heat distribution among the cells.
If a different module shape is assumed, the simulation results would be significantly different.
③

## Slide 26: Results
Composition of air in module
Before venting
Before combustion
During combustion
After combustion
State change of air during thermal runaway progression
Before venting, the temp. of the air slowly increases due to the hot surface of the battery.
After venting start, the inflow of vent gas rapidly raises the air temp. to a level comparable to that of the battery.
Combustion occurs a few seconds after venting start, increasing the air temp. to over 2500 K.
After venting ends and the flame extinguishes, the air temp. rapidly decreases below 500 K.
①
③
④
②

## Slide 27: Results
①
②
① Initiation of vent gas combustion
Accumulated vent gas combusts all at once, releasing large amount of heat in a short period
Flame propagates in air region, consuming oxygen and fuel.
Temperature of gas
Mole fraction of O2

## Slide 28: Results
①
②
Temperature of gas
Chemical heat release rate
② Continous combustion of vent gas
Generated vent gas ignites immediately upon release
Relatively uniform heat generation is achieved.

## Slide 29: Conclusion
Summary
Simulation for TRP is developed by combination of heat generation model, chemical reaction model, and CFD simulation.
Good agreement between heat generation model and chemical reaction model with experimental results
TRP simulation modeled heat transfer from a single cell undergoing thermal runaway to neighboring cells in module.
Thermal runaway propagation mechanism were revealed through analysis of heat transfer path.
Direct conduction was the dominant pathway for thermal runaway propagation, followed by convection and indirect conduction (through plate).
Change of gas composition, gas temperature and propagation of flame is observed.
Future works
1. Validation of simulation through comparison between experimental results will conducted.
2. Surrogate model for the combustion of vent gas needed to investigated.
3. Through parametric study, optimization of battery module / pack design will be conducted.
TRP: Thermal runaway propagation

## Slide 30: Contact Info
Thank you
      Haechan Choi
      Seoul National University
      1, Gwanak-ro, Gwanak-gu, Seoul, Republic of Korea
      +82-10-2492-1528
      Haechan@snu.ac.kr