## Slide 1: Sensitivity Analysis of Various Cooling Methods for Battery Thermal Management Under Fast Charging Conditions Using CFD Simulation
Sangyeop Lee1), Cheolsoo Park2), and Kyoungdoug Min1)
Seoul National University, Seoul, South Korea1)
Hyndai Motor Company2)

## Slide 2: Outline
Introduction
Objective
Methodology
Results
Summary

## Slide 3: Introduction

## Slide 4: Introduction - Growth of EV Adoption
EV adoption expansion and charging infrastructure enhancement for GHG reduction
Increase in EV presence and market share in the auto industry
Greenhouse gases
in the transportation sector
[Government 2050 CNC, 2023]
Chart: 
| 2018 | 2030
계열 1 | 98.1 | 61
98.1 million tons
61.0 million tons
▼ 37.8%
Greenhouse Gas Reduction Goals
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024
전기차 누적 등록 대수 | 9 | 13.5 | 23.1 | 39 | 54.4 | 62.6
친환경차의 비중 | 2.5 | 3.4 | 4.7 | 6.2 | 8.2 | 10.4
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024
전기차 누적 등록 대수 | 9 | 13.5 | 23.1 | 39 | 54.4 | 62.6
친환경차의 비중 | 2.5 | 3.4 | 4.7 | 6.2 | 8.2 | 10.4
Cumulative number of EV registered [ units]
Proportion of
eco-friendly vehicles [%]
[Automobile registration status report, Ministry of Land, Infrastructure and Transport, 2025]
EV Registration Status
EV: Electric Vehicle
GHG: Greenhouse gas

## Slide 5
Introduction - Operating Temperature Range for Li-ion Batteries
[Korthauer, Springer, 2018] [H. Liu, Energy Conversion and Management, 2017]
-20℃
60℃
20℃
40℃
Optimal range
Fast degradation
Transition metal dissolution
Thermal runaway
Lithium plating
Capcity loss
Ionic conductivity decrease
Bernardi equation
In fast charging, rapid increase in current  Quadratic increase in irreversible heat generation
Increased probability of thermal runaway at high temperatures
[Guchen electronics, 2023]
Public
charging pile
3 hours
Fast
charging pile
45 minutes
Ultra-high power
charging station
7 minutes
Increasing Current
 The Necessity of an Advanced Cooling System

## Slide 6
Introduction - Review of Previous Studies
Necessity of gap filler application for contact resistance reduction between cells and cooling plate
Cooling asymmetry caused by the top folding section in pouch cells
Thermal Interface Management
[Xin Ge et al, Royal Society of Chemistry, 2022]
[Lee et al, KSAE, 2024]
Focus of existing sensitivity analyses on coolant conditions such as inlet temperature and flow rate
Definition of objective functions for cooling performance evaluation as maximum temperature and temperature deviation
[M. S. Patil et al, Int J Energy Res, 2020]
[M. Akbarzadeh et al, Applied Thermal Engineering, 2021]
Sensitivity Analysis
Various cooling systems (Air cooling, Indirect cooling, Immersion cooling, PCM cooling)
Research on advanced cooling strategies combining multiple techniques
Cooling Systems
[Offer et al., Nature, 2020]
[Wang Z et al., Journal of Energy Storage, 2023]
Necessity of sensitivity analysis of cooling systems and module components under various cooling methods
Immersion cooling
Indirect cooling
Without gap filler
With gap filler

## Slide 7: Objective

## Slide 8
Objective
ANOVA: Analysis of Variance
Design of experiments using the orthogonal array method
Sensitivity analysis through statistical methods such as range analysis and ANOVA
Comparison of key factors according to different cooling methods
Main Objective
Sensitivity Analysis of Various Battery Cooling System under Fast Charging Conditions
Battery thermal management
Single-sided/Double-sided cooling
Orthogonal array test
Li-ion battery
Computational Fluid Dynamics
Sensitivity analysis

## Slide 9: Methodology

## Slide 10
Methodology - Battery Module Cooling System & Parameters
Module Configuration | 
Battery | NMC Pouch Cell
Cell connection | 2P - 8S
Cooling type | Single/Double-sided
Coolant | Ethylene Glycol-Water mixture
Cell
Pad/Al plate
End plate
Gap filler
Cooling Plate
Coolant
Parameters
Coolant inlet temperature
Coolant mass flow rate
Pad/Al plate ratio
Gap filler thickness
Single-sided cooling system
Double-sided cooling system
Module placed in the straight path
Thickness
Pad
Al plate

## Slide 11
Methodology - Thermal & Battery Modeling
Battery
ECM: Equivalent-Circuit Model
OCV: Open Circuit Voltage
Coolant
Conservation Equations
Turbulence Model | SST K-omega
Flow Model | Segregated Flow
Conjugate Heat Transfer
Bernardi Equation
2RC ECM model
Voltage
Energy Conservation

## Slide 12
Methodology - Simulation set up
SOC: State of Charge
Optimal grid number
 9,600,000
Grid Setting & Independence Test
Material | Grid numbers
Solid | 6,900,000
Fluid | 2,700,000
Load | 2C-rate charge
Cell capacity | 55.6 Ah
SOC range | 20% - 80%
Total time | 1080 s
Ambient/Initial temperature | 25℃
Half – Module Analysis
[]
[]
Cut plane  Adiabatic
Coolant in
Coolant out
Mesh type | Polyhedral mesher
Solid (Cover, Tab) | Thin mesher
Fluid | Prism layer
Time step | 1 s

## Slide 13
Methodology - Key Equations for Analysis Methods
Analysis of Variance
: Number of levels
: Number of level j components
: Sum of squares
: Degree of freedom
[L. Stahle et al, Chemom. Intell. Lab. syst., 1989]
Absolute influence evaluation
Range Analysis
[M. Patil et al, Int J Energy Research, 2020]
: Number of groups
: Number of level j components
Relative influence evaluation
Avg(B) – Avg(A)
Orthogonal Array
Minimal case number
Focus on main effect
Statistical independence of factor combinations
4 Factors x 4 Levels
 L16 Orthogonal Array

## Slide 14
Methodology - Research Flow
Parameter |  | Value
Coolant | Inlet temperature [℃] | 15, 20, 25, 30
 | Mass flow rate [LPM] | Single: 2.5, 5, 7.5, 10
 |  | Double: 1.25, 2.5, 3.75, 5
Pad : Al plate | Ratio | 9:0, 6:3, 3:6, 0:9
Gap filler | Thickness [mm] | 2, 3, 4, 5
Analysis Criteria
(Maximum temperature)
(Temperatere difference)
(Temperature Standard Deviation)
Analysis Criteria
: Maximum battery cell temperature
: Greatest temperature difference across individual cell regions
: Standard deviation of the average temperatures of the battery cells within the module

## Slide 15: Results

## Slide 16
Results - Model Validation with Experiemental Results
Insulation Condition
15℃, 1C rate
25℃, 0.5C/1C rate
Ambient Condition (25℃)
0.5C/1C/1.5C/2C rate
Experiment Cases
▲Ambient Condition
▲Insulation Condition
Insulation Condition
Ambient Condition
0.5C
1C
1.5C
2C
0.5C
1C
1.5C
2C
0.5C
1C, 25℃
1C, 15℃
[Jianqin Wang et al, Applied Thermal Engineering, 2019]
Validation of battery temperature prediction under insulated conditions for heat generation model
Temperature estimation validation under ambient conditions with convective heat transfer
3% temperature and 1% voltage error, indicating model validity

## Slide 17
Higher and in single-sided cooling due to lower heat transfer
Lower top-side heat transfer due to pouch cell folding (double-sided)
Al plate contact shows lower and than pad
Strong inlet-direction effect in single-sided cooling
Increased side heat transfer with higer Al plate ratio  Higher total transfer
Results - Temperature Distribution by Cooling Method
▲Double-Sided Cooling
▲Single-Sided Cooling
47.5%
(77.5W)
52.5%
(85.6W)
115.4 W
Temperature [℃]
▲Double-Sided Cooling
▲Single-Sided Cooling
Pad contact
Pad contact
Al plate contact
Al plate contact
Temperature [℃]

## Slide 18
Results - Range Analysis of Coolant Property Parameters
Double-Sided Cooling
Single-Sided Cooling
33.0 ℃
28.1 ℃
▲Single-Sided Cooling, Coolant Inlet Temperature:30℃
~5 ℃ lower and ~10 ℃ lower in double-sided cooling
Reversal of - trend with decreasing due to lower
Nonlinear behavior at 30 ℃ inlet in single-sided cooling  shift from cooling plate contact to air-exposed cell cover
Reduced drop at higher flow rates (7.5 LPM/3.75 LPM)
Notes: 단면냉각에 비해 양면냉각에서 평균적으로 최고온도는 5도, 온도 편차 10도 정도 낮음
냉각수의 온도가 낮아지면 배터리 셀 내의 최저온도가 낮아져서 오히려 온도 편차가 크게 발생하여 최고온도와 온도 편차의 경향성이 반대로 나타남
동일한 유량 지점을 기준으로 유량을 증가시키더라도 최고온도 감소 효과가 작아짐 (7.5LPM/3.75 LPM)
단면냉각의 입구온도가 25도 일 때의 온도 편차의 경향성이 선형적이지 않음  냉각수 입구온도가 15~25도 일 때는 최저온도가 냉각판과 맞닿는 면에 발생하지만 30도 일 때는 25도의 공기와 접촉하고 있는 cell cover에서 발생하므로 냉각판 하부의 온도보다 더 낮은 온도가 측정된다. 따라서 냉각수 입구온도가 30도일 때 오히려 온도편차가 증가하게 된다.  양면냉각에서는 상부, 하부 모두 냉각수의 영향이 지배적이므로 위와 같은 현상이 발생하지 않는다.  cell cover의 온도는 셀의 안전성에 있어서 크게 중요하지 않으므로 온도 편차를 구하는 방식에 대한 연구가 필요
~5 ℃ lower 𝑇_𝑚𝑎𝑥 and ~10 ℃ lower ∆𝑇 in double-sided cooling vs. single-sided cooling
Inverse trend of 𝑇_𝑚𝑎𝑥 and ∆𝑇 observed with decreasing coolant temperature due to lower 𝑇_𝑚𝑖𝑛 with in cell
Diminished cooling effect at higher flow rates beyond 3.75/7.5 LPM
Nonlinear ∆𝑇 behavior in single-sided cooling at 30 ℃ inlet temperature  Shift of 𝑇_𝑚𝑖𝑛 location from cooling plate surface to air-exposed cell cover increases ∆𝑇  No abnormal ∆𝑇 trend in double-sided cooling due to symmetric coolant influence  Need for reevaluation of ∆𝑇 calculation method considering cell cover’s limited impact on health of battery cell

## Slide 19
Results - Range Analysis of Module Component Parameters
Consistent trends in and across Pad/Al plate ratio and gap filler thickness, redardless of cooling type
Similar sensitivity to both parameters in double-sided cooling; stronger Pad/Al effect in single-sided cooling
Greater sensitivity to Pad/Al ratio than to gap filler thickness in both cooling types
Sharp drop when gap filler thickness decreases from 3mm to 2mm (both cooling types)
Single-Sided Cooling
Double-Sided Cooling

## Slide 20
Results - Range Analysis Comparison
Coolant inlet temperature: key factor for and  More effective in double-sided ( ) and single-sided () cooling
Pad/Al plate ratio: more impact in single-sided cooling ( & )  Single-sided cooling: higher ratio of lateral heat transfer
Gap filler thickness: more impact in double-sided cooling ( & )  Double-sided cooling: higher ratio of top/bottom heat transfer  Gap filler acting as a major bottleneck, resulting in greater influence
T -
M -
P:A -
d -
E -
4.45
2.88
0.36
0.26
3.22
1.37
0.54
1.06
0.27
0.10
7.62
11.35
0.62
0.65
3.20
1.36
1.24
1.76
0.25
0.15
Notes: <1>
최고온도, 온도편차는 냉각수 입구온도가, 셀 간 온도의 표준편차는 pad:al plate 비율이 가장 지배적임
냉각수 입구온도는 최고온도를 낮추기 위해서는 양면냉각에서 더 효과적이며, 온도 편차를 줄이기 위해서는 단면냉각에서 더 효과적임
gap filler 두께는 단면보다 양면에서 더 효과적임
최고온도에 대해서 단면냉각에서는 pad:al plate 비율이 gap filler 두께보다 영향도가 더 컸지만, 양면냉각에서는 그 반대임
온도편차와 온도 표준편차에 대해서는 단면냉각과 양면냉각의 영향도 순위가 동일함
parameter의 범위에 따라서 달라질 수 있기 때문에 유의성을 따지기 위해서는 anova 해야함
<2>
Coolant inlet temperature: key factor for 𝑇_𝑚𝑎𝑥 and ∆𝑇;  More effective in double-sided (𝑇_𝑚𝑎𝑥 ) and single-sided (∆𝑇) cooling
𝑇_𝑚𝑎𝑥 와 ∆𝑇 둘 다에 대해서 Pad/Al plate 비율은 single-sided cooling에 영향을 더 크게 미치는 반면, gap filler thickness는 double-sided cooling에 영향을 더 크게 미침
전체 열전달량에 대해서 측면으로 나가는 열전달량의 비율이 single-sided에서 더 크기 때문에 방열물질에 영향을 더 크게 받음
전체 열전달량에 대해서 상부와 하부로 나가는 열전달량은 double-sided에서 더 크며, gap filler는 상/하부 열전달의 큰 bottle neck 이므로 single-sided에 비해 큰 영향을 받음

## Slide 21
Results - Range Analysis Comparison
Consistent trend in across cooling types
Single-sided cooling shows ~0.2℃ higher , greater sensitivity to parameter variation
Pad/Al plate ratio is the most dominant factor for , but the relationship is non-linear  With the same heat dissipating materials, inner cells are hotter and outer cells are cooler  6:3 ratio (6 Pads): Temperature of Cell 1▼, Cell 8▲  reduced  3:6 ratio (6 Al plates): Temperature of Cell 1▲, Cell 8▼  increased
0.13
0.08
0.01
0.01
0.22
0.13
0.05
0.03
0.00
0.01
T -
M -
P:A -
d -
E -
Cut plane
▲All-Pad case
1
2
3
4
5
6
7
8

## Slide 22
Results - Analysis of Variance
,  Coolant inlet temperature > Pad : Al plate > Gap filler thickness > Mass flow rate
 Coolant inlet temperature > Gap filler thickness > Pad : Al plate > Mass flow rate
 Pad : Al plate > Coolant inlet temperature > Gap filler thickness > Mass flow rate
[Jianqin Wang et al, Applied Thermal Engineering, 2019]
Variance for factor j () < Twice the Variance for test error (2)  Very small factor effect  Minimal factor effect of mass flow rate on (single-sided) and (double-sided)
Variance |  |  |  |  |  | 
 | Single | Double | Single | Double | Single | Double
Coolant inlet temperature | 43.4006 | 95.2530 | 14.1410 | 6.2454 | 0.0119 | 0.0044
Coolant mass flow rate | 0.3868 | 0.3670 | 0.0922 | 0.0481 | 8.6405 e-5 | 4.1540 e-5
Pad: Al plate ratio | 7.5276 | 1.3925 | 7.4121 | 1.4488 | 0.0327 | 0.0117
Gap filler thickness | 1.1541 | 2.3383 | 0.1995 | 0.8015 | 0.0024 | 5.6791 e-4
Error | 0.0563 | 0.0219 | 0.0628  0.0775 | 0.01 | 5.3991 e-6 | 1.1496 e-4  7.8248 e-5
Variance |  |  |  |  |  | 
 | Single | Double | Single | Double | Single | Double
Coolant inlet temperature | 43.4006 | 95.2530 | 14.1410 | 6.2454 | 0.0119 | 0.0044
Coolant mass flow rate | 0.3868 | 0.3670 | 0.0922 | 0.0481 | 8.6405 e-5 | 4.1540 e-5
Pad: Al plate ratio | 7.5276 | 1.3925 | 7.4121 | 1.4488 | 0.0327 | 0.0117
Gap filler thickness | 1.1541 | 2.3383 | 0.1995 | 0.8015 | 0.0024 | 5.6791 e-4
Error | 0.0563 | 0.0219 | 0.0628  0.0775 | 0.01 | 5.3991 e-6 | 1.1496 e-4  7.8248 e-5

## Slide 23
Results – Analysis of Variance
Coolant inlet temperature and Pad:Al plate ratio  99.5% confidence for , , and
Coolant inlet temperature - key for thermal safety
Pad:Al plate ratio – key for reducing cell-to-cell variation
Mass flow rate < 90% confidence for
Gap filler thickness > 99.5% confidence for &  Greater significance in double-sided cooling
T -
M -
P:A -
d -

## Slide 24: Summary

## Slide 25
Dominant influence of coolant inlet temperature on , regardless of cooling method  Critical for maintaining ideal battery operating temperature
Primary impact of Pad : Al plate ratio on independent of cooling method  Essential for preventing battery lifespan due to cell imbalance
Highlighted importance of Pad : Al plate ratio in single-sided and gap filler thickness in double-sided cooling
Generally low influence of mass flow rate acrossing cooling methods
Sensitivity analysis of key parameters’ influences on single & double sided cooling methods
Summary & Future Works
Summary
Future Works
Sensitivity analysis on new parameters such as Pad:Al plate arrangement and coolant channel placement
Further investigation into meaningful performance metrics for evaluating battery cooling effectiveness
Optimization based on analysis of cost-related factors such as pump power and mass in cooling system design

## Slide 26
Thank you for listening
      Sangyeop Lee
      Seoul National University, Seoul, South Korea
      saltlake9707@snu.ac.kr
      Sensitivity Analysis of Various Cooling Methods for Battery Thermal Management Under Fast Charging Conditions Using CFD Simulation

## Slide 27: Appendix

## Slide 28
90.5 %
Appendix - Heat Transfer Ratio between Top Side and Bottom Side
Cell
Cooling plate
Gap filler
Fin Side
Normal Side
<Experiment>
<Simulation>
90 %
Fin Side
Normal Side

## Slide 29
Appendix - Pad : Al plate Arrangement
Cell
Pad
Al plate
Pad : Al plate = 6:3
Cut Plane
Outside
Pad : Al plate = 3:6
Cut Plane
Outside

## Slide 30
Appendix - Error Calculation Methods
Inclusion of an artificial error factor with designated levels
Execution of range anlaysis based on results for each error level
Estimation of error based on variation across error levels
Range Analysis Error
Analysis of Variance Error
Estimation of error through variance among cases at the same level of factor j
Level 1
Level 2
Level 3
Avg (Level 1)

## Slide 31
Appendix - Analysis of Variance
F - Value |  |  |  |  |  | 
 | Single | Double | Single | Double | Single | Double
Coolant inlet temperature | 771.43 | 4355.90 | 182.49 | 625.81 | 2203.90 | 55.67
Coolant mass flow rate | 6.87 | 16.78 | 1.19 | 4.82 | 16.00 | 0.53
Pad: Al plate ratio | 133.80 | 63.68 | 95.66 | 145.17 | 6052.22 | 149.10
Gap filler thickness | 20.51 | 106.93 | 2.57 | 80.31 | 435.85 | 7.26
F - Value |  |  |  |  |  | 
 | Single | Double | Single | Double | Single | Double
Coolant inlet temperature | 771.43 | 4355.90 | 182.49 | 625.81 | 2203.90 | 55.67
Coolant mass flow rate | 6.87 | 16.78 | 1.19 | 4.82 | 16.00 | 0.53
Pad: Al plate ratio | 133.80 | 63.68 | 95.66 | 145.17 | 6052.22 | 149.10
Gap filler thickness | 20.51 | 106.93 | 2.57 | 80.31 | 435.85 | 7.26
Variance |  |  |  |  |  | 
 | Single | Double | Single | Double | Single | Double
Coolant inlet temperature | 43.4006 | 95.2530 | 14.1410 | 6.2454 | 0.0119 | 0.0044
Coolant mass flow rate | 0.3868 | 0.3670 | 0.0922 | 0.0481 | 8.6405 e-5 | 4.1540 e-5
Pad: Al plate ratio | 7.5276 | 1.3925 | 7.4121 | 1.4488 | 0.0327 | 0.0117
Gap filler thickness | 1.1541 | 2.3383 | 0.1995 | 0.8015 | 0.0024 | 5.6791 e-4
Error | 0.0563 | 0.0219 | 0.0628 | 0.01 | 5.3991 e-6 | 1.1496 e-4
Variance |  |  |  |  |  | 
 | Single | Double | Single | Double | Single | Double
Coolant inlet temperature | 43.4006 | 95.2530 | 14.1410 | 6.2454 | 0.0119 | 0.0044
Coolant mass flow rate | 0.3868 | 0.3670 | 0.0922 | 0.0481 | 8.6405 e-5 | 4.1540 e-5
Pad: Al plate ratio | 7.5276 | 1.3925 | 7.4121 | 1.4488 | 0.0327 | 0.0117
Gap filler thickness | 1.1541 | 2.3383 | 0.1995 | 0.8015 | 0.0024 | 5.6791 e-4
Error | 0.0563 | 0.0219 | 0.0628 | 0.01 | 5.3991 e-6 | 1.1496 e-4
[Jianqin Wang et al, Applied Thermal Engineering, 2019]
= 5.3908
= 9.2766
= 29.4567
= 47.4672
= 3.2888
= 4.7571
= 9.7795
= 12.9166

## Slide 32
Appendix - Pump Power
Other Parameters
Level 1
Level 2
Level 3
Level 4