## Slide 1: Research on improving safety of using R290 refrigerant in future xEVs 2nd report
Kunihiko Hayashi, Yoshiaki Miyazato,
Tomoki Shimizu

## Slide 2: Contents
Background and Motivation
Study scenario
Result
3-1. Garage concentration test
3-2. Cabin intake test
3-3. Behavior and effects of gas leak into cooling loop
Conclusion

## Slide 3: Contents
Background and Motivation
Study scenario
Result
3-1. Garage concentration test
3-2. Cabin intake test
3-3. Behavior and effects of gas leak into cooling loop
Conclusion

## Slide 4: Background and Motivation
Potential EU PFAS ban may require alternative Natural refrigerants
This study will focus on propagation of R290 (Propane) in event of a leak.
 | Refrigerant | EU PFAS definition | Heating |  | Cooling |  | Standard (for Auto) | Flammability | System cost
 |  |  | Performance | COP | Performance | COP |  |  | 
Current | R1234yf | × | 〇 | 〇 | 〇 | 〇 | 〇 | A2L | 〇
Natural Refrigerant | CO2 (R744） | 〇 | 〇+ | 〇+ | 〇 | 〇ーー | 〇 | ー | 〇ー ～×
自然冷媒 | Propane （R290） | 〇 | 〇 | 〇+ | 〇+ | 〇ー | N/A | A3 | 〇ー

## Slide 5: System Safety Approach
Flammable
mixture
Ignition
source
Frequency
Risk
Risk factor
Minimize Risk by controlling ignition sources, flammable mixtures, and frequency
OEM/Supplier
SAE CRP activities
Align with SAE CRP activities (team entropy), support SNAP applications and J-Std.
Based on standards like ISO26262, make safety systems fail-safe.
Considering risk and safer system solutions, this study focuses on flammable mixture.

## Slide 6: Contents
Background and Motivation
Study scenario
Result
3-1. Garage concentration test
3-2. Cabin intake test
3-3. Behavior and effects of gas leak into cooling loop
Conclusion

## Slide 7: Study scenario
Cabin
battery
R/T
R/T
R/T
Under-hood
Condenser
Refrigerant cycle
Chiller #1
Chiller #2
Heater core
Cooler core
Bulkhead
安全性：故障時のFHリスク
Considered: ① Vehicle outside and ②Cabin, ③Cooling loop leak scenarios
◆Possible gas leak route
Radiator
HEX
Reserve Tank
W/P
HVAC
Assumption: Parked in the small garage
③Into the Cooling loop
①Outside of the vehicle
②Into the Passenger Cabin

## Slide 8: Contents
Background and Motivation
Study scenario
Result
3-1. Garage concentration test
3-2. Cabin intake test
3-3. Behavior and effects of gas leak into cooling loop
Conclusion

## Slide 9: Consideration point
Understanding the behavior and impact of leaked gas in the small garage
Verification of the radiator e-fan effect to mitigate concentration gas
Verified CFD/vehicle test about leakage gas concentration in the small garage
1. Measure concentration
Environmental conditions: small garage
2900mm
5700mm
Leaked gas
2. e-Fan effect
Concentration
9.5％
2.1％
Flammable
concentration
Concentration [Vol.％]
Target area
Notes: 検討では、停車時の厳しめ環境として、米国で一般的な密閉空間である、小型ガレージを設定しております。
ガレージは横2900×高さ5700の車両1台が入る小型のもので、後方にシャッターを想定し、隙間を設定します。
検討項目はガレージ内の漏洩ガス挙動と濃度把握に加え、
漏洩時の安全基準確率に役立つよう、ラジエータファン駆動による効果を検証します。
漏洩ガス濃度としては、可変範囲下限なる、2.1%が基準となります。

## Slide 10: CFD/Vehicle testing conditions
CFD and actual vehicle tests are conducted.
At the 2nd report, slow leak situation is added.
CFD | Vehicle test | Charge amount [g] | Leak Rate [g/s] | Leak Location | Radiator e-Fan
〇 | 〇 | 150 | 13.5 (Fast leak) | Center | Off
〇 | 〇 | 150 | 13.5 | Center | On(max)
〇 | 〇 | 300 | 13.5 | Center | Off
〇 | 〇 | 300 | 13.5 | Center | On(max)
〇 | 〇 | 600 | 13.5 | Center | Off
〇 | 〇 | 600 | 13.5 | Center | On(max)
〇 | 〇 | 600 | 0.034 (Slow leak) | Center | Off
〇 | 〇 | 600 | 0.034 | Center | Off
1st
report
2nd
report

## Slide 11: CFD condition
Garage door alternative slit
（3mm×2025mm)
Verifying surface
(Vehicle center)
【CFD condition】 Star CCM+
Analysis method: Multicomponent gas CFD
(Transient analysis)
Analysis period：0～300 s
Initial: Air 100 %
Propane inflow: 13.51 g/s
e-fan speed：0 or max Speed
Verifying gas diffusion in the Garage using 3D-CFD
Vehicle: bZ4X
Garage size: 5.7×2.9×2.5m
0.61m
0.3m
5.7m
2.5m
Vehicle front

## Slide 12: CFD Result: Gas leak comparison with/without e-Fan
With e-fan, the flammable gas is diffused, and the flammable range is reduced.
No Fan, Refrigerant: 300g
Colored: Above 1/4 LFL、 Black: Above LFL
Leakage after 10sec
60sec
300sec
Leakage after 10sec
60sec
300sec
with e-Fan: Max , Refrigerant: 300g

## Slide 13: Vehicle test condition
Garage leakage scenario evaluation based on SAE setting
◆Camera/Sensor location
(*) sensor: 100mm height from floor level
(*) sensor making and validation conducted by SOKEN inc.
Leak point
item | condition
Leak location | Above the eAxle
Test gas | CO2
Gas Direction | Upper direction
Leak amount | 150,300,600g
Leak rate | 13.5、0.034g/s
e-Fan | Off, On(max speed)
①
②
④
Sensor
#2
#3
#4
#5
#6
#1
③
5700mm
2900mm
Camera
bZ4X
◆Test condition
◆Gas leaked position
(Under-hood)
CO2Gas supply device
CO2 Cylinder
CO2
Blower
×10 Speed
Notes: 車両設置条件を示します。
CFD同様、PCUユニット上方にガスを上向きに噴出、漏洩量は150,300,600gとし、
漏洩速度は事故相当の、非常に速い漏洩量となります。
右の動画でガス漏洩状況を透明にしたボンネットで示します。
ガスはボンネットに当り、下方に流れます。
この挙動を、車両中心に設置した濃度センサと、側面に設置したカメラで確認します。
About gas leakage to outside, we had conducted garage concentration test.
This is the test condition.
We used a tent as garage for this verification.
Space size is same as CFD.
For this verification, CO2 gas is used because of safety.

## Slide 14: Concentration sensor
・Use of CO2 as an alternative gas
・Building a gas concentration sensor to understand gas behavior
◆Gas concentration sensor: NDIR
CO2
受光部
(フォトセンサ)
CO2波長の吸収量違いを
測定⇒濃度算出
ガス濃度に応じて減衰
CO2 波長のみ限定
中赤外 LED
赤外線
BPフィルタ
(*) sensor making and validation conducted by SOKEN inc.
Gas concentration detection using infrared absorption method
Mid-infrared LED
Band Pass Filter
4300ー200nm
Gas flow
D34
W56
H46
Photo Sensor
(Non-Dispersive InfraRed)
Detection accuracy: ±0.5pt
Known Gas Concentration[vol%]
Sensor output
Accuracy:
Accuracy: ±0.2pt
(@LFL)
Notes: 実車評価では、冷媒ガス挙動の可視化に加え、冷媒ガス濃度の計測が必要になります。
計測機器はSOKEN様開発のシステムを活用しております。
左に示す可視化装置では、代替ガスとなるCO2ガスにスモーク発生器トレーサを混ぜる装置を使用しました。
トレーサはプロピレングリコールを活用し、ストークス数を基準に、ラジエータファン作動範囲で流れに追従できることを確認しております。
右に示すガス濃度測定では、赤外線吸収法を活用したセンサを新たに開発いただき、
検出精度としては、想定する上限の最大10%濃度までで±0.5pt、着火下限の2%付近では0.2ptの精度を確立いただいております。
For the concentration testing, we used NDIR sensor made by SOKEN.
Using mid-infrared LED and Band Pass Filter limited to only CO2 wavelength, the light receiving section can measure the difference in CO2 wavelength absorption.
About this sensor, max measurement variation is less than 0.5% concentration.

## Slide 15: Result: Gas leakage in the Garage (with/without e-Fan)
With e-fan, 600g flammable gas is diffused to below LFL at 300sec.
Gas concentration (under the Vehicle, 100mm Hight)
LFL
Time[s]
Concentration[Vol%]
Leak
Gas amount: 600g, No Fan
Above LFL after leak.
LFL
Time[s]
Concentration[Vol%]
Fan ON (entire time)
Leak
①
②
③
④
⑥
⑤
Vehicle front
Rear
Sensor
100mm
Gas amount: 600g, Fan ON
Rear sensor measure above LFL after 30sec, then diffused to below LFL at 300sec.
Stop
Stop

## Slide 16: Charge amount vs. Concentration (Vehicle test)
Charge Amount[g]
Concentration[Vol%]
Fast Leak : Leak After 300sec
Slow Leak : Leak stop timing
Height = 100mm
(*)Highest concentration point
LFL
Fan ON(Fast leak)
No Fan(Fast leak)
No Fan(Slow leak)
Leak
speed
effect
e-Fan
effect
Fast
Slow
With fan ON and less than 600g charge, Concentration is below LFL at leak 300s
At slow leak condition, until 600g do not exceed LFL limit with no fan
【Leak speed】
Fast leak: 15.3g/s
Slow leak: 0.034g/s
No fan
fan ON

## Slide 17: Contents
Background and Motivation
Study scenario
Result
3-1. Garage concentration test
3-2. Cabin intake test
3-3. Behavior and effects of gas leak into cooling loop
Conclusion

## Slide 18: Vehicle test condition (Cabin intake test)
Radiator
e-Fan
Recirculation
Fresh
Leaked gas
Passenger
Cabin
HVAC
Verified Cabin intake after gas leakage in under-hood
Concentration
measurement
9.5％
2.1％
Flammable
concentration
Concentration [Vol.％]
Target area
① Face
② Foot
Sensor Location
(*) made by SOKEN inc.
Mid-infrared LED
Band Pass Filter
Gas flow
Photo Sensor
NDIR sensor
Vehicle: Toyota bZ4X
Garage size: 5.7×2.9×2.5m
 | Condition
Leak location | Above the eAxle
Test gas | CO2
Sensor | NDIR
Gas Direction | Upper direction
HVAC | Fresh/Recirc,(Blower ON)
Notes: 検討では、停車時の厳しめ環境として、米国で一般的な密閉空間である、小型ガレージを設定しております。
ガレージは横2900×高さ5700の車両1台が入る小型のもので、後方にシャッターを想定し、隙間を設定します。
検討項目はガレージ内の漏洩ガス挙動と濃度把握に加え、
漏洩時の安全基準確率に役立つよう、ラジエータファン駆動による効果を検証します。
漏洩ガス濃度としては、可変範囲下限なる、2.1%が基準となります。

## Slide 19: Vehicle testing conditions
Understanding gas intake to cabin at under-hood leak situation
 | Charge amount [g] | Leak Rate [g/s] | Leak Location | Radiator e-Fan | HVAC |  | 
 |  |  |  |  | Mode | Direction | Blower
1 | 150 | 13.5(Fast) | Center | Off | Fresh | Foot | High
2 | 150 | 13.5 | Center | On(max) | Fresh | Foot | High
3 | 300 | 13.5 | Center | Off | Fresh | Foot | High
4 | 300 | 13.5 | Center | On(max) | Fresh | Foot | High
5 | 600 | 13.5 | Center | Off | Fresh | Foot | High
6 | 600 | 13.5 | Center | On(max) | Fresh | Foot | High
7 | 600 | 13.5 | Center | Off | Recirc | Foot | High
8 | 600 | 13.5 | Center | On(max) | Recirc | Foot | High
9 | 600 | 0.034(Slow) | Center | Off | Fresh | Foot | High
10 | 600 | 0.034 | Center | On(max) | Fresh | Foot | High
11 | 600 | 0.034 | Center | On(max) | Recirc | Foot | High
Test Vehicle
(bZ4X)
Gas and smoke
Delivery system
① Face
② Foot
Sensor Location
(*) made by SOKEN inc.
Mid-infrared LED
Band Pass Filter
Gas flow
Photo Sensor
NDIR sensor
(*)Test gas: CO2

## Slide 20: ① Comparison : Fresh/Recirc , and Fan On/Off (Fast Leak)
～300sec
Overall
600g, Foot sensor
300
Time[sec]
10000
Time[sec]
Concentration[vol%]
Concentration[vol%]
Fan Off(Fresh)
Fan On(Fresh)
Fan On(Recirc)
Fan Off(Recirc)
Fan Off(Fresh)
LFL
Blower
Stopped
LFL
Fan On(Recirc)
Fan Off(Recirc)
Fan On(Fresh)
Blower
Stopped
・Fresh: Peak is above LFL at 600g leak. Fan Off increase higher concentration after Blower Off.
・Recirc: Peak is below LFL at same leak. After stopping HVAC blower, Fan On is higher than Off.

## Slide 21: ② Comparison : Fresh/Recirc (Slow Leak, Fan On)
Recirc
Fresh
Time[Hr]
Concentration[vol%]
Concentration[vol%]
Time[Hr]
LFL
LFL
foot
face
foot
face
600g, 0.034g/s(Slow Leak)
At up to 600g leak, Recirc mode can prevent from above LFL, even if after Blower stopping
300g
600g
300g
600g
Blower
Stopped
Blower
Stopped

## Slide 22: Charge vs. concentration in the Cabin
Foot sensor
Face sensor
Fan On
LFL
Fan Off
(Fresh)
(Fresh)
Fan On
Fan Off
Fan On
(Recirc)
Fan On
(Recirc)
～300s
Blower stopped
～300s
Blower stopped
LFL
・More then 150g fast leak with Fresh mode, Concentration Peak around floor level is above LFL.
・Recirc mode prevent above LFL.
・Increased Concentration after blower stopped is needed to take care.
Fan On
(Recirc)
Fan On
Peak Concentration[vol%]
Peak Concentration[vol%]

## Slide 23: Contents
Background and Motivation
Study scenario
Result
3-1. Garage concentration test
3-2. Cabin intake test
3-3. Behavior and effects of gas leak into cooling loop
Conclusion

## Slide 24: Gas leakage into cooling loop
Coolant
Refrigerant
Leak amount
Corrosion pinhole
Relief valve prevent over pressure
Gases Phase
Refrigerant Leak
Liquid Phase
refrigerant Leak
Coolant
Refrigerant
Liquid Phase
Gases Phase
Refrigerant
Coolant
Liquid Phase
Gases Phase
This study
(Future work)
Liquid Phase
Refrigerant ratio
Plate type heat exchanger does not usually occur large leak into coolant side
High probability case
Worst
Case
Assumption:
Hose burst
（image）
Cooling Loop
Spring
Valve Seal
Relief valve structure
Reserve tank cap
Relief Valve
Gas flow
too much refrigerant leak could affect frozen because of the latent heat
Consideration point: Verifying hose burst or destruction, frozen because of the leak

## Slide 25: Gas leakage into cooling loop
Reserve tank
Relief valve
Cap
13pixel
Initial(0kPa)
Valve lift(108kPa)
1mm
Visualization of Relief valve
Added
Window
Relief valve
Valve seal
Based on visualization of relief valve, vilifying whether frozen would be happen or not.
Heater
core
HEX
Reserve tank
Flow mater
W/P
Pressure
sensor
Cite glass
Camera
Camera
 |  | Condition
Environment | Initial temperature | -30,-20,-10,0,20,40
Coolant | Concentration ratio | Ethylene Glycol/Water 50％
 | Flow rate | 5L/min
Coolant loop and visualization point
Refrigerant
leak

## Slide 26: Result: Gas leakage into cooling loop
Low temp.
①Pressure
②Valve lift (-18℃)
-18℃
0℃
Heater core
HEX
Reserve tank
W/P
Pressure sensor
Visualization of Cite glass
Refrigerant
leak
Extremely
Small amount
No frozen
High leak
Atmosphere/Refrigerant/Coolant temp. vs. valve lift
Cite glass
0.17mm
Initial(0kPa)
During relief(108kPa)
5mm
+10kPa
At gases phase leak situation, relief valve frozen, hose burst and disruption do not occur
-10℃
No abnormal rise, normal operation

## Slide 27: Contents
Background and Motivation
Study scenario
Result
3-1. Garage concentration test
3-2. Cabin intake test
3-3. Behavior and effects of gas leak into cooling loop
Conclusion

## Slide 28: Conclusion
(1) Garage concentration test
・With fan on and less than 600g charge, Concentration is below LFL at fast leakage.
・Concentration is below LFL at slow leakage condition without fan.
(2) Cabin intake test
・Recirculation mode prevent from higher intake of leakage gas from under-hood.
・Concentration increased after blower turning off.
(3) Bench test of gas leakage into cooling loop
・There was no frozen situation based on gases phase refrigerant leak into cooling loop.
・The cooling loop relief valve prevents potential hose disconnections or bursts from gas leaks under test conditions.

## Slide 29: Contact Info
Thank you!
      Name : Kunihiko Hayashi
      Company : TOYOTA MOTOR CORPORATION
      Address : Mishuku 1200, Susono-shi, Shizuoka-ken
      Phone : (+81)50-3166-9408
      Email : kunihiko_hayashi@mail.toyota.co.jp