## Slide 2: Alternative Refrigerant and Refrigeration/Heat Pump Systems
JAEMIN LEE, BONGHO KANG, JISEONG NOH, HYERI KIM
SK innovation

## Slide 3: Contents
Background
SK refrigerants
System performance test
SK Oil solution for stability
SAE CRP Process
Conclusion

## Slide 4: Background
Environmental Regulations
R-134a
R-1234yf
F-gas
Regulation
PFAS
Regulation
New Refrigerant
Meet all regulation
High GWP
PFAS Concerns
Heat pump capacity for EV
Low temp.
Thermal
management
Applying heat pumps
for efficiency
Reduced heat pump performance at low temp.
Need for improvement
Amb. Temp
HP capacity
Gen. 3 Refrigerant
Gen.4 Refrigerant
Next Gen.
Need for new refrigerants
Insufficient
refrigerant

## Slide 5: SK Refrigerants
New Refrigerants Meeting Market Needs
 System compatibility
 Regulations
 System performance
 Toxicity/Flammability
Category | R-1234yf | R-744 (CO2) | R-290 (Propane) | R-494B | R-4101A
Composition | Single | Single | Single | Ternary | Ternary
① Regulations | ● (PFAS concerns) | ● | ● | ● | ●
② Toxicity/Flammability | ● | ● | ● (flammability) | ● | ●
③ System compatibility | ● | ● (High pressure system) | ● (in-direct system) | ● | ●
④ System performance | ● | ● | ● | ● | ●
Comparison of Alternative Refrigerants for Automobile HVAC
● Good ● Acceptable ● Concerns

## Slide 6: SK Refrigerants
Property | R-494B | R-4101A | R-1234yf
Composition (wt%) | CF3I / R-152a / R-744 (58 / 38 / 4) | CF3I / R-152a / R-32 (58.5 / 30.5 / 11) | -
GWP | 48 | 113 | ~1
Environmental | Non-PFAS | Non-PFAS | PFAS TFA concerns
ASHRAE Classification | A2L | A2L | A2L
Boiling point (℃) (@1barA) | -48.5 | -39.2 | -29.5
Dew Point (℃) (@1barA) | -29.5 | -31.7 | -29.5
Critical Temperature (℃) | 107.6 | 102.9 | 94.7
Temp. Glide (@20bar) | 12.2 | 5.9 | 0.0
Both refrigerants are A2L replacements for R-1234yf MVAC system allowing existing system architectures
No refrigerant ignition observed when exposed to various automotive electrical ignition sources
Risk assessment expected to show lower risk of fire due to refrigerant ignition compared to R1234yf
SK refrigerants have suitable properties to offer superior heating performance in low ambient

## Slide 7: SK Refrigerants - PFAS
Definition of PFAS
EU&OECD : “Any substance that contains at least one fully fluorinated methyl (CF3-) or methylene (-CF2-) carbon atom without any H/Cl/Br/I attached to it.”
US State (Maine and Minnesota) : one fully fluorinated carbon molecule (Includes HFOs and most other F-gases except few such as R32, R152a, CF3I)
SK Refrigerants are PFAS-Free.
R-152a (Not PFAS)
Name : 1,1-Difluoroethane
Chemical Formula : C2H4F2
CAS No. : 75-37-6
CF3I (Not PFAS)
Name : Trifluoroiodomethane
Chemical Formula : CF3I
CAS No. : 2314-97-8
R-744 (Not PFAS)
Name : Carbon Dioxide
Chemical Formula : CO2
CAS No. : 124-38-9
Non-Fluorine
R-32 (Not PFAS)
Name : Difluoromethane
Chemical Formula : CH2F2
CAS No. : 75-10-5

## Slide 8: SK Refrigerants - Properties
R-1234yf
R-494B
Designed properties for System Performance Improvement
Operating range
Extension of
heating operating range
Enthalpy properties
Saturation Curve
Extension of enthalpy range
Designed with similar saturation curve to R1234yf for system compatibility
Add R4101A
Plan to be update
Temperature(℃)
120
80
40
0
-40
-80
Cooling
Heating
R-1234yf
R-494B
R-4101A
Cooling
Heating
R-4101A
△enthalpy ↑
Dew point
Bubble point
R-1234yf
R-494B
R-4101A
R-744

## Slide 9: SK Refrigerants – thermodynamic performance simulation
Name | Class | GWP (AR4) | Cap Cooling | COP Cooling | Cap Heating | COP Heating | Pdisch | Full Glide (K) | Evap. Glide (K) | Cond. Glide (K)
R-1234yf | A2L | <1 | 100% | 100% | 100% | 100% | 100% | 0.0 | 0.0 | 0.0
R-494B | A2L | 48 | 133% | 107% | 139% | 113% | 119% | 17.6 | 4.9 | 12.8
R-4101A | A2L | 113 | 139% | 108% | 150% | 113% | 120% | 7.2 | 4.2 | 6.1
Cooling: Tcd=55 ℃, Tev=-2 ℃, Subcooling:5 ℃, Superheat:10 ℃, Isentropic Eff: 70%
Heating: Tcd=65 ℃, Tev=-30 ℃, Subcooling:5 ℃, Superheat:10 ℃, Isentropic Eff: 70%
R-494B and R-4101A show superior performance compared to R-1234yf
Discharge pressure within 20% of R1234yf suggesting no change required in design of components
R494B and R4101A are expected to offer superior performance compared to R1234yf under drop-in conditions

## Slide 10: System performance test- hyundai ioniq5 model
Refrigerant | Oil | Ref. mass (g) | Oil mass (g)
R-1234yf | ENEOS POE | 1200 | 240
R-494B | SK Oil | 1420 | 190
R-4101A | SK Oil | 1450 | 200
SK internal system assessment equipment
Test specimen : Hyundai Ioniq 5 heat pump system and component.
e-Compressor : Scroll type, 45cc volume
Mode | Amb. Temp (℃) | Veh. Speed (kph) | Air flow rate (CMH)
Cooling | 45 | 50 | 530
Heating | -20 | 50 | 350
 | -7 | 50 | 350
1) Oil Circulation Rate : Oil content in the refrigerant/oil mixture
Test equipment
Test conditions
Heat pump schematic
※ Oil mass is determined based on an OCR1) of 3-5%

## Slide 11: System performance test- hyundai ioniq5 model
Improved cooling performance with SK refrigerants
Chart: 
| Q-Evap (kW) | COP
R1234yf(8600rpm) | 5.9 | 1.09
R-494B(4600rpm) | 5.83 | 1.67
R-4101A(4200rpm) | 5.89 | 1.74
53%↑
Ambient temperature (45℃)
Same capacity
59%↑
Cooling mode

## Slide 12: System performance test- hyundai ioniq5 model
Chart: 
| Q-heat (kW) | Pwr consumption (kW)
R1234yf(3700rpm) | 2.46 | 8.29
R-494B(5350rpm) | 3.46 | 7.97
R-4101A(4500rpm) | 3.16 | 7.9
Chart: 
| Q-heat (kW) | COP | Pwr consupmtion (kW)
R1234yf(3700rpm) | 2.46 | 2.55 | 8.29
R-494B(2970rpm) | 2.47 | 2.81 | 8.2
R-4101A(2830rpm) | 2.44 | 3.14 | 8.12
10%↑
Heating mode
Reduced heating power consumption through improved heating performance
Heating (-20℃)
Same capacity
23%↑
1%↓
2%↓
41%↑
28%↑
4%↓
5%↓
1)
1) Total PTC power consumption for target discharge temperature of 60°C
Increase Comp. RPM until the low-side pressure reaches atmospheric.
1)

## Slide 13: System performance test- hyundai ioniq5 model
Chart: 
| Q-heat (kW) | Pwr consumption (kW)
R1234yf(3700rpm) | 3.34 | 4.9
R-494B(5350rpm) | 4 | 4.54
R-4101A(4500rpm) | 4.02 | 4.46
Chart: 
| Q-heat (kW) | COP | Pwr consupmtion (kW)
R1234yf(3700rpm) | 3.34 | 2.48 | 4.9
R-494B(2970rpm) | 3.36 | 2.77 | 4.74
R-4101A(2830rpm) | 3.31 | 2.9 | 4.72
12%↑
Heating mode
Reduced heating power consumption through improved heating performance
Heating (-7℃)
Same capacity
17%↑
3%↓
4%↓
20%↑
20%↑
7%↓
9%↓
1)
1) Total PTC power consumption for target discharge temperature of 50°C
Increase Comp. RPM to match R1234yf
1)

## Slide 14: System performance test- hyundai KONA EV model
Refrigerant | Oil | Ref. mass(g) | Oil mass(g)
R1234yf | ENEOS POE | 1675 | 300
R-494B | SK Oil | 2095 | 325
Evaluation conducted at Creative Thermal Solutions (CTS) (partner of SAE CRP)
Test specimen : Hyundai KONA heat pump system and component.
e-Compressor : Scroll type, 33cc volume
Test equipment
Test conditions
SAE J 2765 Reduced Matrix
Cooling and heating mode was conducted respectively
1) Oil Circulation Rate : Oil content in the refrigerant/oil mixture
※ Oil mass is determined based on an OCR1) of 3-4%
Heat pump schematic

## Slide 15: System performance test- hyundai KONA EV model
SAE Full test matrix
Reduced test matrix
Cooling
Heating

## Slide 16: System performance test- hyundai KONA EV model
Reduced test matrix
No. | Test Name | Outdoor |  | indoor |  |  | Bat.
 |  | Amb. Temp | Veh. speed | HX Temp Air in | RH | Target Temp. HX Air Out | Target Load
 |  | ℃ | Km/h | ℃ | % | ℃ | kW
1 | I10a | 10 | 0 | 10 | 80 | 5C/45C | 0
2 | H10a | 10 | 120 | 10 | 80 | 5C/45C | 1.5
3 | I25c | 25 | 0 | 25 | 50 | 3 | 0.1
4 | I25c-8 | 25 | 0 | 22 | 40 | 8 | 0.1
5 | I25a | 25 | 0 | 25 | 80 | 3 | 0.1
6 | H25a | 25 | 120 | 25 | 80 | 3 | 1.5
7 | I35a | 35 | 0 | 35 | 40 | 3 | 0.1
8 | H35a | 35 | 120 | 35 | 40 | 3 | 2
9 | H35b | 35 | 120 | 25 | 50 | 8 | 2
10 | I45 | 45 | 0 | 35 | 25 | 3 | 0.1
11 | M45 | 45 | 80 | 35 | 25 | 3 | 1
No. | Test Name | Outdoor |  | indoor |  | 
 |  | Amb. Temp | Veh. speed | HX Temp Air in | RH | Target Temp. HX Air Out
 |  | ℃ | Km/h | ℃ | % | ℃
1 | M-20a | -20 | 80 | -20 | - | 55
2 | I-20c | -20 | 0 | 10 | - | 55
3 | H-20c | -20 | 120 | 10 | - | 55
4 | M-10a | -10 | 80 | -10 | - | 55
5 | I-10c | 10 | 0 | 15 | - | 55
6 | H-10c | -10 | 120 | 15 | - | 55
7 | M0a | 0 | 0 | 0 | - | 55
8 | I0b | 0 | 0 | 10 | - | 55
9 | H0b | 0 | 120 | 10 | - | 55
Cooling (11 conditions)
Heating (9 conditions)

## Slide 17: System performance test- hyundai KONA EV model
Chart: COP
| I10a | H10a | I25c | I25c-8 | I25a | H25a | I35a | H35a | H35b | I45 | M45
R1234yf | 3.77 | 4.12 | 2.81 | 3.87 | 3.16 | 2.05 | 2.66 | 1.95 | 2.75 | 2.01 | 1.47
R-494B Capacity match to yf | 3.39 | 3.72 | 3.08 | 2.95 | 3.11 | 2.88 | 3.09 | 2.53 | 3.06 | 2.36 | 1.94
Cooling test results
COP of R494B (equivalent AC capacity to R1234yf)
Improves COP at the same AC capacity as R1234yf.
Ambient increase
Grater capacity relative to yf

## Slide 18: System performance test- hyundai KONA EV model
Chart: COP
| M-20a | I-20c | H-20c | M-10a | I-10c | H-10c | M0a | I0b | H0b
R1234yf | 1.21 | 1.3 | 1.44 | 1.42 | 1.46 | 1.77 | 1.38 | 1.65 | 1.97
R-494B Capacity match to yf | 1.27 | 1.31 | 1.51 | 1.53 | 1.57 | 1.88 | 1.84 | 1.87 | 2.27
Heating test results
Achieves higher heating capacity than R1234yf in HP mode.
Reduces COP for heating at the same heating capacity as R1234yf.
Ambient increase
COP of R494B (equivalent AC capacity to R1234yf)

## Slide 19: SAE CRP Process
    4Q
【 SAE CRP Process】
2024
2026
    1Q
2025
    2Q
    3Q
    4Q
    1Q
    2Q
    3Q
2023
Phase#1
Phase#3
Phase#2
FTA (Fault Tree Analysis)
Target date : ‘25.3Q
Risk assessment
System Testing
Thermal stability
Initial screening
0d Calculation
LCCP analysis
To be completed after the LCCP tool release
SNAP Submission

## Slide 20: Conclusion
Performance enhancement
System compatibility
R494B and R4101A offer low GWP and non PFAS alternatives for automotive applications
SK Ref.
Regulation
Toxicity
Flammability
Compliant with GWP and PFAS environmental regulations
R-494B,R-4101A ASHRAE A2L Approval
(Not flammable in nominal composition and WCF1) condition)
Operational compatibility confirmed in Kona EV and Ioniq 5.
Long-term compressor durability testing in progress
Increased cooling and heating performance for HP system with R1234yf.

## Slide 21: Conclusion – Tech. road map
Short term
Mid term
Long term
Development of alternative refrigerants and oils for Vehicles
Development of new refrigerants materials
Total refrigerants solution company
Expansion of Applications
Residential and Industrial HVAC applications
Data Centers and ESS applications

## Slide 22: Contact info.
      Name : JAEMIN LEE
      Company : SK Innovation
      Address : 325 Expo-ro, Yuseong-gu, Daejeon, South Korea 34124
      Phone : +82-010-2352-2686
      Email : jmin2@sk.com

## Slide 23
Thank you