## Slide 2: Learnings from R290 System Development
Dana Nicgorski
Thermal Systems Engineering Director
Robert Bosch LLC

## Slide 3: Learnings from R290 System Development
Bosch thermal system portfolio for R290
Thermal Systems Research Lab - Waltham, MA USA
Oil circulation & solubility vs performance
Importance of thermal isolation with compact systems
Influence of vapor injection
Vapor injection vs hot gas at -30°C
Single vs dual-chiller systems
Paper # (if applicable)

## Slide 4: Bosch Thermal System Portfolio for R290
Paper # (if applicable)
Heat Pump Unit (HPU)
Integrated heat pump for R290
Safety-oriented integration concept
Smart Oil Actuator (SmA )
Oil flow rate control
Sensor-less and self-locking
Cooling Fan
12 or 48V
Best in class NVH
Cooling Fan
HPU
FTU-C
TMC
FTU-O
TMC (TM Software Controller)
Thermal management controls for coolant, refrigerant, and cabin
Innovative predictive features
Flexible Thermal Units for Coolant (FTU-C)
Flexible packaging and functionality supports customer specific integration
Scalable hydraulic power
FTU-O (eAxle oil cooling system)
Efficient waste heat recovery
Incl. all devices for oil cooling circuit
Today’s presentation will focus on learnings from R290 HPU system development
SmA

## Slide 5: Thermal Systems Research Lab – Waltham MA
Paper # (if applicable)
Thermal System Lab in climate chamber enables fundamental investigations of system design and performance / controls impacts
Climate Chamber in Vehicle Lab
ECF
HVAC
Temp. range | -30°C to 55°C
Max chamber cooling | 20 kW
Bat, eAxle
Simulators
System
Interactions
Wallboard w/ R290 System & Coolant Topology
R290 System
(Before Insulation)

## Slide 6: Oil Circulation & Solubility vs Performance
Paper # (if applicable)
Early energy balance studies showed a ~8% performance reduction due to oil circulation rate (OCR) vs analysis done with pure R290  OCR must be considered in all analysis to produce realistic predictions
In simplest terms, when calculating enthalpy w/ pure R290 based on 10 K superheat:
  a 2% oil circulation rate “steals” 7.9 kJ/kg of enthalpy in the superheat region
  A 4% oil circulation rate “steals” 16.8 kJ/kg of enthalpy in the superheat region
1) Ossorio et. al, Impact of Lubricant in the in the Evaporator as a Function of Oil Circulation Rate in Variable Speed Heat Pumps working with R290, 2022
Coriolis Massflow Sensor
P-h-X diagram of R290 and POE68 (OCR=5%)1
Pure R290
w/ oil
R290 Boiling Out of PAG

## Slide 7: Importance of Thermal Isolation
Paper # (if applicable)
Energy balance checks of early samples showed ~500 W of imbalance correlating best with chiller temp.  Care must be taken to avoid thermal short-circuits during system development
LCC
Chiller
Heat
flows
~12 regressions of test data explored
Only parameters related to chiller temp showed a trend
2x outliers ignored

## Slide 8: Influence of Vapor Injection (VI)
Paper # (if applicable)
Chiller/Condenser Inlet Temp (°C)
-30
-20
-10
35
53
Vapor Injection
Base System
Too High Discharge Temps
+8%
+5%
+7%
+5%
VI enables system operation at -30°C and produces a ~8% to ~15% lever on speed or capacity
TCO of VI vs increasing eCom cc, hot gas cycle or HV heater will be OEM and use-case dependent
Inlet T | -30°C |  | -20°C |  | -10°C |  | 35°C |  | 53°C | 
System | Base | VI | Base | VI | Base | VI | Base | VI | Base | VI
RPM | n/a | 8408 | 6863 | 5727 | 6379 | 5562 | 5988 | 5494 | 6245 | 5495
Speed | n/a |  | -17% |  | -13% |  | -8% |  | -12% | 
Noise (dBA) | n/a |  | -1.1 |  | -2.5 |  | -2.3 |  | -1.9 | 
Q Heat / Cool (kW) | 5.5 |  | 5.5 |  | 7 |  | 10 |  | 10 | 
eComp
Chiller
Economizer
R/D
LCC

## Slide 9: Vapor Injection vs Hot Gas Cycle at -30°C (-22°F)
Paper # (if applicable)
Vapor Injection outperformed Hot Gas time to 43°C LCC inlet from -30°C for all Bosch tests
eCom load is developed sooner with VI, allowing system to begin heating the coolant/cabin sooner despite lower peak heating capacity. COP ~2.3x higher with VI over entire startup
 | Vapor Injection | Hot Gas
Time to 43°C LCC Coolant Inlet Target | 15.6 min | 17.3 min
Preheat Pump Off Time | 6.7 min | 8.7 min
% Time Heating Coolant | 59% | 45%
Avg HT Delivered to Coolant (Pump On) | 3.72 kW | 4.37 kW
Calculated Energy delivered to Coolant | 570 Wh | 570 Wh
Avg start-up COP incl. Preheating | 0.56 | 0.24
eComp
Chiller
R/D
LCC
eComp
Chiller
Economizer
R/D
LCC
R290 “Dryness”
Governed
*
*

## Slide 10: Single vs Dual Chiller Systems (1/2)
Paper # (if applicable)
R290 Circuit
Coolant Circuit
Single Chiller
Dual Chiller
Parallel Heat Sources
(Cabin + Batt)
Isolated Heat Sources
(Cabin + Batt)
from a Tesla Model X
90° travel, 90 discrete steps
Chiller Coolant Mixing Valve
536 discrete steps
Two Evap. EXVs
 Single and dual chiller systems were studied with a focus on the battery + cabin dual cooling use case

## Slide 11: Single vs Dual Chiller Systems (2/2)
Paper # (if applicable)
…576
90°= 90 Steps
Single Chiller
Dual Chiller
7.8 kW system capacity
(10.3 kW w/ VI)
10.7 kW system capacity
 Both systems are controllable to the limit of the refrigerant system capacity. Coolant valve had 11 mixing control steps and the EXV had 25 steps
 Dual-chiller system had 2x chiller coolant flow and heat transfer area, which raised cooling capacity
System | ΣQ (kW) | ΣFlow (LPM) | Delta T (K) | Total COP | Volume
Single | 7.8 | 21.3 | 5.9 | 1.06 | 100%
Single w/ VI | 7.6 | 21.2 | 5.8 | 1.19 | 100%
Dual | 7.6 | 40 | 3.4/2.7 | 1.22 | 200%

## Slide 12: Contributors
Special thanks to:
Brandon Dryer
Elliot Ko
Parry, Eleanor, Gianna, Max and the many NEU Co-Ops that supported building and operating the Thermal Systems Research lab
Paper # (if applicable)

## Slide 13: Contact Info
Thank you
      Dana Nicgorski
      Robert Bosch LLC
      101 1st ave. Waltham MA 02451
      +1-781-684-5325
      Dana.Nicgorski@us.bosch.com
Paper # (if applicable)