## Slide 2: Enhanced R290 System
IL YOUNG PARK

## Slide 3: Contents
Indirect Thermal Management System
Precedent Research
Rationales of Enhanced Approach
Test Facility Schematic
Components Information
Test Result
Wrap-up

## Slide 4: Indirect Thermal Management System
With increasing of electrical parts in vehicle, Indirect Thermal Management System would be more suitable way to handle it
simplified refrigerant cycle with secondary loop of coolant
Direct System | Indirect System
Complex refrigerant loop, relatively simple coolant loop
Costly due to more refrigerant components
Cooling performance designed to meet traditional A/C control
Some reliability risk from complex refrigerant system and control
Not always to achieve optimal performance
Simple refrigerant loop, complex coolant loop
Cost saving at vehicle level
Similar cooling performance with new control strategy
Low reliability risk due to simple refrigerant system and control
Easier to reach optimal COP
Comp
Chiller
LCC
VI - H
VI-M
Coolant
Loop
Coolant
Loop
Comp
Evap
Chiller
OHX
I.Cond
Comp
Evap
Chiller
I.Cond
LCC
Comp
Chiller
LCC
IHX - H
IHX - L
Coolant
Loop
Coolant
Loop
The Economizer cycle also use Internal Heat Exchanger. To distinguish two concepts,
in this study, IHX using for economizer is referred to as “VI cycle”
Economizer
- IHX Cycle -
- VI Cycle -

## Slide 5: Proper Refrigerant for Indirect System
From the perspective of low GWP and operating envelop, R290 would be suitable fluid having higher energy efficiency
Property | R134a (HFC) | R1234yf (HFO) | R290 (HC)
Status of Application | Being phased out | Current Standard | Growing adoption
GWP | 1,430 | 4 (or <1 in some sources) | 3
Flammability (Class) | None (A1) | Mild (A2L) | High (A3)
Toxicity | Non-toxic | Low toxicity | Non-toxic
Energy Efficiency | Moderate | Comparable to R134a | High
Tc = 70C, P = 2586 kPa
Te = -3C, P = 432 kPa
Pr = 5.99
Δh = 199 kJ/kg
Td = 99C
Tc = 70C, P = 2044 kPa
Te = -3C, P = 284 kPa
Pr = 7.17
Δh = 74 kJ/kg
Td = 84C

## Slide 6: Precedent Research
R1234yf vs. R290
Better refrigerant property (large phase change) leads similar chiller
performance even if running with lower refrigerant mass flow rate(34%)
Ps 410 kPaA
Ps 220 kPaA
Pd 1770 kPaA
22.4g/s
ePower 3.26kW
Pr 5.5
R1234yf
R290
66.0g/s
ePower 4.69kW
Pr 8.0
SC7K
SC7K
Td 105.5C
Td 99.4C
Pd 2230 kPaA
Refrigerant | COP | Liquid Cool Condenser |  | Chiller |  |  | Qc [kW]
 |  | Tw_in [C] | Vol. Flow [LPM] | Tw_in [C] | Tw_out [C] | Vol. Flow [LPM] | 
R1234yf | 1.20 | 53 | 16 | 4.0 | -0.7 | 20 | 5.6
R290 | 1.67 |  |  |  |  |  | 
-2.0C
-4.2C
-2.5C
-4.5C
Pressure [kPaA]
Optimal Operation (w/ R1234yf)
Optimal
Operation
Qc1 = Qc2 = Qc3
Qc1
Qc2
Qc3
: Find best COP points with sub-cool control
Sanhua US internal test result
Enthalpy [kJ/kg]

## Slide 7: Rationales of Enhanced Approach by IHX cycle
Theoretical Review
IHX HP
IHX LP
LCC
Chiller
Comp
EXV
- ∆TSC increases potential capacity of chiller(∆h)
: can get more cooling capacity (= ∆Q)
- Higher inlet(∆TSh) & discharge temp of compressor
: may need additional input comp work (= ∆W)
- Increased ∆Td extends heating capacity
w/o increasing condensation pressure
vs
* A/C control with required Q @ limited Tw,in of heat sink
actual operating status
- H/X starting from lower quality (xin’) @chiller-in
allows to get the same Qc with higher Teva (or Ps)
- Lower Pr(compression load) reduces input work
(∆W < 0)
+ IHX

## Slide 8: Rationales of Enhanced Approach by VI cycle
VI (vapor injection) Cycle
1) Additional Sub.cool(∆SC) increases potential capacity of chiller(∆h)
2) Additional mass flow rate (mi) increases heating capacity
3) Reduced input power (W - W’ = ∆W) increases COP
4) Reduced discharge temp (∆Td) enlarges operating envelop
LCC
Chiller
Comp
EXV 1
Economizer
EXV 2

## Slide 9: Indirect Thermal Management System
IHX System
VI System
Baseline
IHX
ECO

## Slide 10: Components Information
Liquid Cool Condenser
Chiller
Vapor Injection Compressor
Size [mm3] | 141 x 70 x 84 (L x W x H)
Refrigerant Side | Dimple
 | I-flow
 | 1Path 30R
Coolant Side | Fin
 | I-flow
 | 1Path 31W
Size [mm3] | 168 x 78 x 89 (L x W x H)
Refrigerant Side | Fishbone
 | I-flow
 | 3 Path 8,13,21R
Coolant Side | Fishbone
 | I-flow
 | 1 Path 43W
Displacement [cc] | 34
Refrigerant | R290
Package (D X L) [mm] | 241 x 200 x 180
Weight [kg] | 7.15
Max. ePower [kW] | 10
Input Voltage [Vdc] | 180 ~ 470V 400 ~ 900V
Speed Range [rpm] | 800 ~ 8500
Oil | PAG RFL68EP
Leakage [g/yr] | 5

## Slide 11: Charge Determination Test
Charge Determination Test
- Test condition
. Max. Cabin Cooling Condition
. R290 Charging : 150 to 350g
. 34cc eComp running with PAG Oil
. Temp @LCC out : 53 ~ 60 degC
. Pressure @Comp out : 19 ~ 24 barA
 | Refrigerant
Baseline | 178g
IHX Cycle | 200g
VI Cycle | 310g
Proper Charging
e.g) Vapor Injection Case

## Slide 12: Test Result Summary
 | Liquid Cool Condenser |  |  | Chiller |  | Capacity
 | Mode | Flow Rate | Temp In | Flow Rate | Temp In | 
 |  | [LPM] | [°C] | [LPM] | [°C] | [kW]
Cooling Mode | A | 20 | 45 | 20 | 5 | 3.5
 | B |  | 35 |  | 10 | 7.6
 | C |  | 53 | 23 | 8.3 | 8.3
 | D |  | 60 |  |  | 8.0
Heating Mode | A | 16 | 48 | 12 | -20 | 6.3
 | B |  | 65 |  | -8 | 7.9
Test Condition
Cooling Mode
Heating Mode

## Slide 13: Test Result – 1) IHX vs VI
Cooling “B” Mode
Heating “B” Mode
- Additional mass flow rate of VI function would be helpful to meet required
heating capacity at LCC even if running with lower comp speed
 @ H/P mode, VI performance seems better than IHX behavior
- Heat transfer from heat source to refrigerant with lower inlet quality @chiller,
would be more helpful to improve cycle performance than VI function
 @ A/C mode, IHX seems better option to enhance performance.
Qheat 7.9 kW
Qcool 7.6 kW
COP 103%
COP 112%
COP 100%
COP 112%
COP 100%
COP 100%
ePower 90%
ePower 101%
ePower 100%
ePower 97%
ePower 90%
ePower 100%
74% rpm
101% rpm
100% rpm
91% rpm
91% rpm
100% rpm

## Slide 14: Test Result – 2) IHX sizing effect
Test Configuration
: Testing for IHX Sizing effect with controlling IHX bypass flow
IHX HP
IHX LP
LCC
Chiller
Comp
EXV
All of data points make same cooling capacity
Proper IHX sizing @Mild Load:0.5kW, @High Load : 2.0kW ↑
@Mild Load, after 55 steps, Chiller exit changed to gas out
Gas phase out
Gas phase exit leads degradation of cooling cycle efficiency
Optimal operation
Large IHX
Small IHX

## Slide 15: Test Result – 3) VI Characteristic
* 2016, Purdue University, International Compressor Engineering Conference, A Methodology for Characterization of Vapor injection Compressors
Injection point property can be estimated by regression formular of pressure ratio and mass flow ratio
Finding vapor injection point property in the cycle by correlated parameters*

## Slide 16: Wrap-up
Enhanced approach of IHX and VI in R290 secondary loop cycle were evaluated and compared quantitively
- Cooling Mode : IHX cycle would be better application for enhancing performance
- Heating Mode : VI cycle would be better application for enhancing performance
Through the evaluation of the IHX sizing effect, it would be able to propose suitable IHX sizing for the system
Based on the VI evaluation with various conditions, VI characteristics in the cycle can be estimated with formula of injection pressure ratio and mass flow rate
* Review
* Future Work
Considerations on how to reduce R290 refrigerant charging amount
Operating Envelop Testing of R290 Cycle

## Slide 17: Contact Info
      Name : ILYOUNG PARK
      Company : Sanhua Automotive
      Address : 3729 Auburn Rd, Auburn Hills, MI,US, Zip:48360
      Phone : 248-402-3328
      EMail : young.park@sanhuagroup.com
Paper # (if applicable)